Chapter 4 Measurement units and conversion factors

This is a preliminary text for the chapter. The Oslo Group is invited to provide comments on the

general structure and coverage of the chapter (for example, if it covers the relevant aspects related to

measurement units and conversion factors, and if there are additional topics that should be covered in

this chapter), and on the recommendations to be contained in IRES.

The current text presents the recommendations from the UN Manual F.29 as well as some points that

were raised during the last OG meeting. The issue of “harmonization” of standard/default conversion

factors still needs to be addressed. It was suggested that tables be moved to an annex. Please provide

your views on which ones should be retained in the chapter.

A. Introduction

4.1. Energy products are measured in physical units by their weight or mass, volume, and energy.

The measurement units that are specific to an energy product and are employed at the point of

measurement of the energy flow are often referred to as “original” or “natural” units (IEA/Eurostat

Manual page 19). Coal, for example, is generally measured by its mass or weight and crude oil by its

volume. In cross-fuel tabulations such as the energy balances energy sources and commodities are also

displayed in a “common unit” to allow comparison across sources. These “common” units are usually

energy units and require the conversion of a quantity of a product from its original units through

application of appropriate conversion factors.

4.2. When different units are used to measure a product, the compiler is left with the task of

converting units which, in absence of specific information on the products (such as density, gravity and

calorific value), may lead to different figures.

4.3. This chapter provides a review of the physical measurement units used for energy statistics,

explains the concepts of original and common units, discusses the importance of conversion factors for

the conversion from original to common units and presents standard conversion factors to use in

absence of country- or region-specific conversion factors.

B. Measurement units

4.4. Energy sources and commodities are measured by their mass or weight, volume, and energy.

This section covers the “original” or “natural” units as well as the common units. It also makes

reference to the International System of Units – often abbreviated as SI from the French “Système

International d’Unités” – which is a modernized version of the metric system established by

international agreement. It provides a logical and interconnected framework for all measurements in

science, industry and commerce. The SI is built upon a foundation of seven base units plus two

supplementary units. Multiples and sub-multiples are expressed in the decimal system. See Box 4.1for

more details on SI.

IRES

2

4.5. Standardization in the recording and presentation of original units is a primary task of an energy

statistician before quantities can be analyzed or compared. (UN Manual F.44 page 11).

Box 4.1: International System of Units

1. Original units

4.6. As mentioned in para 4.1, original units are the units of measurement employed at the point of

measurement of the product flow that are those best suited to its physical state (solid, liquid or gas) and

that require the simplest measuring instruments (IEA/Eurostat Manual page 19). Typical examples are

mass units for solid fuels (e.g. kilograms or tons) (with some exceptions, for example, for fuelwood

which is usually sold in stacks and measured in a local volume unit, then converted to cubic metres) and

volume units for liquids and gases (e.g. litres or cubic metres). The actual units used nationally vary

according to country and local condition and reflect historical practice in the country, sometimes

adapted to changing fuel supply conditions (IEA/Eurostat Manual page 177).

4.7. Electricity is measured in kilowatt-hour (kWh), an energy unit (although it is rather a unit of

work) which allows one to perceive the electrical energy in terms of the time an appliance of a specified

wattage takes to “consume” this energy. Heat quantities in steam flows are calculated from

measurements of the pressure and temperature of the steam and may be expressed in calories or joules.

Apart from the measurements to derive the heat content of steam, heat flows are rarely measured but

inferred from the fuel used to produce them.

4.8. It should be noted that it may occur that, in questionnaires for the collection of energy statistics,

data may be required to be reported in different units from the original/natural unit for certain classes of

fuels. For example, statistics on crude oil and oil products may be requested in a mass or weight basis

since the heating value of oil products by weight displays less variation than the heating value by

volume. Statistics on gases, as well as wastes, can be requested in terajoules or other energy unit in

order to ensure comparability, since gases (and wastes) are usually defined on the basis of their

production processes, rather than their chemical composition and different compositions of the same

type of gas (or waste) entail different energy contents by volume. Collection of statistics on wastes in

an energy unit should be based on the measured or inferred heat output. It is important to note that

energy statistics on waste refer only to the portion used for energy purposes.

Mass units

4.9. Solid fuels, such as coal and coke, are generally measured in mass units. The SI unit for mass is

the kilograms, kg. Metric tons (tons) are most commonly used - for example, to measure coal, oil and

their derivatives. One ton corresponds to 1000 kg. Other units of mass used by countries include:

pound (0.4536 kg), short ton (907.185 kg) and long ton (1016.05 kg). Table 1 presents the equivalent

factors to convert different mass units.

DESCRIPTION TO BE INSERTED

IRES

3

Table 1: Mass equivalents

Kilograms Metric INTO tons Long tons Short tons Pounds

FROM MULTIPLY BY

Kilograms 1.0 0.001 0.000984 0.001102 2.2046

Metric tons 1000. 1.0 0.984 1.1023 2204.6

Long tons 1016. 1.016 1.0 1.120 2240.0

Short tons 907.2 0.9072 0.893 1.0 2000.0

Pounds 0.454 0.000454 0.000446 0.0005 1.0

Note: The units of the columns can be converted into the units of the rows by dividing by the

conversion factors in the table.

Example: Convert from metric tons (ton) into long tons: 1 ton = 0.984 long ton.

Volume units

4.10. Volume units are original units for most liquid and gaseous, as well as for some traditional

fuels. The SI unit for volume is the cubic metre which is equivalent to a kilolitre or one thousand litres.

Other volume units include: the British or Imperial gallon (4.546 litres), United States gallon (3.785

litres), the barrel (159 litres) and the cubic feet, which is also used to measure volumes of gaseous fuels.

Given the preference from oil markets for the barrel as a volume unit, the barrel per day is commonly

used within the petroleum sector so as to allow direct data comparison across different time frequencies

(e.g., monthly versus annual crude oil production). However, in principle other units of volume per time

can be used for the same purpose. Table 2 shows the equivalent factors to convert volume units.

Table 2: Volume equivalents

U.S.

gallons Imperial gallons Barrels Cubic feet Litres Cubic

metres

INTO

FROM MULTIPLY BY

U.S. gallons 1.0 0.8327 0.02381 0.1337 3.785 0.0038

Imp. gallons 1.201 1.0 0.02859 0.1605 4.546 0.0045

Barrels 42.0 34.97 1.0 5.615 159.0 0.159

Cubic feet 7.48 6.229 0.1781 1.0 28.3 0.0283

Litres 0.2642 0.220 0.0063 0.0353 1.0 0.001

Cubic metres 264.2 220.0 6.289 35.3147 1000.0 1.0

Note: The units of the columns can be converted into the units of the rows by dividing by the conversion factors in the table.

Example: Convert from barrels into cubic meters. 1 barrel = 0.159 cubic meter.

Conversions between mass and volume - Specific gravity and density

4.11. Since liquid fuels can be measured by either weight or volume it is essential to be able to

convert one into the other. This is accomplished by using the density of the liquid. Specific gravity is

the ratio of the mass of a given volume of oil at 15°C to the mass of the same volume of water at that

temperature. Density is the mass per unit volume.

Mass oil mass

Specific gravity=

mass water Density=

volume

IRES

4

4.12. When density is expressed in kilograms per litre, it is equivalent to the specific gravity. When

using the SI or metric system, in order to calculate volume, mass is divided by the specific gravity or

density; and, vice versa, to obtain mass, volume is multiplied by the specific gravity or density. When

using other measurement systems, one must consult tables of conversion factors to move between mass

and volume measurements.

4.13. Another frequently used measure to express the gravity or density of liquid fuels is API gravity,

a standard adopted by the American Petroleum Institute. API gravity is related to specific gravity by

the following formula:

141.5

API gravity =

specific gravity

- 131.5

4.14. Thus specific gravity and API gravity are inversely related. They are both useful in that specific

gravity increases with energy content per unit volume (e.g. barrel), while API gravity increases with

energy content per unit mass (e.g. ton).

Energy units

4.15. Energy, heat, work and power are four concepts that are often confused. If force is exerted on

an object and moves it over a distance, work is done, heat is released (under anything other than

unrealistically ideal conditions) and energy is transformed. Energy, heat and work are three facets of

the same concept. Energy is the capacity to do (and often the result of doing) work. Heat can be a byproduct

of work, but is also a form of energy. Consider an automobile with a full tank of gasoline.

Embodied in that gasoline is chemical energy with the ability to create heat (with the application of a

spark) and to do work (the gasoline combustion powers the automobile over a distance).

4.16. The SI unit of energy, heat and work is the joule (J). Other units include: the kilogram calorie

in the metric system, or kilocalorie, (kcal) or one of its multiples; the British thermal unit (Btu) or one

of its multiples; and the kilowatt hour (kWh).

4.17. Power is the rate at which work is done (or heat released, or energy converted). A light bulb

draws 100 joules of energy per second of electricity, and uses that electricity to emit light and heat (both

forms of energy). The rate of one joule per second is called a watt. The light bulb, operating at 100 J/s,

is drawing power of 100 Watts.

4.18. The joule is a precise measure of energy and work. It is defined as the work done when a

constant force of 1 Newton is exerted on a body with mass of 1 gram to move it a distance of 1 metre.

One joule of heat is approximately equal to one fourth of a calorie and one thousandth of a Btu.

Common multiples of the joule are the megajoule, gigajoule, terajoule and petajoule.

4.19. The gram calorie is a precise measure of heat energy and is equal to the amount of heat

required to raise the temperature of 1 gram of water at 14.5C by 1 degree Celsius. It may also be

referred to as an International Steam Table calorie (IT calorie). The kilocalorie and the teracalorie are

its two multiples which find common usage in the measurement of energy commodities.

4.20. The British thermal unit is a precise measure of heat and is equal to the amount of heat required

to raise the temperature of 1 pound of water at 60°F by 1 degree Fahrenheit. Its most used multiples are

the therm (105 Btu) and the quad (1015 Btu).

IRES

5

4.21. The kilowatt hour is a precise measure of heat and work. It is the work equivalent to 1000 watts

(joules per second) over a one hour period. Thus 1 kilowatt-hour equals 3.6x106 joules. Electricity is

generally measured in kilowatt hour.

2. Common units

4.22. The original units in which energy sources and commodities are most naturally measured vary

(e.g. tons, barrels, kilowatt hours, therm, calories, joules, cubic metres), thus quantity of energy sources

and commodities are generally converted into a common unit to allow, for example, comparisons of

fuel quantities and estimate efficiencies. The conversion from different units to a common unit requires

some conversion factors for each product. This is addressed in Section C of this chapter.

4.23. The energy unit in the International System of Units is the joule which is very commonly used

in energy statistics. Other energy units are also used such as: the ton of oil equivalent (TOE) (41.868

gigajoules), the Gigawatt-hour (GWh), the British thermal unit (Btu) (1055.1 joules) and its derived

units – therm (1015 Btu) and quad (105 Btu) - and the teracalorie (4.205 joules).

4.24. In the past, when coal was the principal commercial fuel, the ton of coal equivalent (TCE) was

commonly used. However, with the increasing importance of oil, it has been replaced by the ton of oil

equivalent. Table 3 shows the conversion equivalents between the common units.

Table 3: Conversion equivalents between energy units

TJ Million INTO Btu GCal GWh MTOE

FROM MULTIPLY BY

Terajoule 1 947.8 238.84 0.2777 2.388x10-5

Million Btu 1.0551x10-3 1 0.252 2.9307x10−4 2.52x10−8

GigaCalorie 4.1868x10-3 3.968 1 1.163x10−3 10-7

Gigawatt hour 3.6 3412 860 1 8.6x10-5

MTOE 4.1868x104 3.968x107 10-7 11630 1

Note: The units of the columns can be converted into the units of the rows by dividing by the conversion factors

in the table.

Example: Convert from Gigawatt-hours (GWh) into Terajoules (TJ): 1 GWh = 3.6 TJ.

C. Calorific values

[the standard factors displayed in the tables are from the UN manual F. 44. They need to be

reviewed and discussed]

4.25. The compilation of overall energy balances, as opposed to the balance of a single energy

product (also referred to in energy statistics as a commodity balance), requires conversion of the original

units in which the fuel are measured to a common unit of measurement. In addition, it may also be

necessary to apply some form of conversion for certain individual fuels (e.g. to express different grades of

coal in terms of coal of a standard calorific content). Even though conversion factors are often considered in

the context of the preparation of energy balances, they have wider application in the preparation of any

tables designed to show energy in an aggregated form or in the preparation of inter-fuel comparative

analyses.

IRES

6

4.26. Calorific value or heating value of a fuel express the heat obtained from one unit of the fuel.

They are obtained by measurements in a laboratory specializing in fuel quality determination. They

should preferably be in terms of joules (or any of its multiples) per original unit, for example

gigajoule/ton (GJ/t) or gigajoule/cubic metre (GJ/m3). Major fuel producers (mining companies,

refineries, etc.) measure the calorific value and other qualities of the fuels they produce.

4.27. There are two ways of expressing calorific values: gross or net of the latent heat of the water

formed during combustion and previously present in the form of moisture. Also, the calorific values

depend on the quality of the energy product: the calorific value of a ton of hard coal may vary greatly

by geographic and geological location; thus they are specific to the fuel and transaction in question.

These two issues are discussed in detail in the next two sections.

1. Gross and net calorific/ heating values

4.28. The expression of original units of energy sources in terms of a common unit may be made on

two bases as the energy stored in fuels may be measured in two stages. The gross calorific value

(GCV), or high heat value, measures the total amount of heat that will be produced by combustion.

However, part of this heat will be locked up in the latent heat of evaporation of any water present in the

fuel before combustion (moisture) or generated in the combustion process. This latter comes from the

combination of hydrogen present in the fuel with the oxidant oxygen (O2) present in the air to form

H2O. This combination itself releases heat, but this heat is partly used in the evaporation of the

generated water.

4.29. The net calorific value (NCV), or low heat value, excludes this latent heat. NCV is that amount

of heat which is actually available from the combustion process for capture and use. The higher the

moisture of a fuel or its hydrogen content, the greater is the difference between GCV and NCV. For

some fuels with very little or no hydrogen content (e.g., some types of coke, blast furnace gas), this

difference is negligible. The applied technology to burn a fuel can also play a role in determining the

NCV of the fuel, depending for example on how much of the latent heat it can recover from the exhaust

gases.

4.30. In 1982, in the UN Manual F.29, it was recommended that:

“When expressing the energy content of primary and secondary fossil energy sources in terms of

a common energy accounting unit, net calorific values (NCV) should be used in preference to

gross calorific values (GCV). If and when recuperation of a significant part of the difference

between GCV and NCV from exhaust gases becomes a practical possibility and seems likely to

become a reality, this recommended basis may need to be reconsidered (para. 135, UN Manual

F.29).

4.31. This recommendation was made based on practical considerations:

“With present technologies, the latent heat from the condensation of water vapour cannot be

recovered from exhaust gases. If these gases were to be cooled below a certain level, they

would not rise out of a boiler chimney and the reduced air current would either reduce boiler

efficiency or would call for the use of energy in driving a fan to force the gases out of the

chimney. Condensation of water would cause corrosion problems with sulphur dioxide (SO2)

and other residues. Yet, another practical consideration is that the natural moisture content of

solid fuels depends greatly on the occurrence of rainfall during transport and storage, so that

NCV is a better indication of the energy effectively obtainable from combustible fuels when

making comparisons through time and between countries (unless the moisture content of solid

fuels is reduced to a standard level before GCV is measured). (Para 133 UN Manual F.29)

IRES

7

4.32. Given that new technologies may have been developed in the generation of energy to capture

the latent heat, for example in gas-fired condensing boilers, it may be possible to recommend the use of

GCV instead of NCVs.

4.33. In terms of magnitude, the difference between gross and net calorific values of commercial

energy sources (coal, oil, products, and gas) is less than 10 per cent while that of traditional energy

(fuelwood, bagasse) is usually more than 10 per cent. Figures for the main energy commodities are

presented below in Table 4.

Table 4: Difference between net and gross calorific values for selected fuels

Fuel Percentage

Coke 0

Charcoal 0 – 4

Anthracite 2 – 3

Bituminous coals 3 – 5

Sub-Bituminous coals 5 – 7

Lignite 9 – 10

Crude oil 8

Petroleum products 7 – 9

Natural gas 9 – 10

Liquified natural gas 7 – 10

Gasworks gas 8 – 10

Coke-oven gas 10 – 11

Bagasse (50% moisture content) 21 – 22

Fuelwood (10% moisture content) 11 – 12

(20% moisture content) 22 – 23

(30% moisture content) 34 – 35

(40% moisture content) 45 – 46

Sources: This is taken from the UN Manual F. 44 and the original source was :[T. T. Baumeister and

others, eds., Marks Standard Handbook for Mechanical Engineers (McGraw Hill, New York, 1978); United

States of America, Federal Energy Administration, Energy Interrelationships (Springfield, Virginia, National

Technical Information Service, 1977); United Nations, Economic Commission for Europe, Annual Bulletin of

Gas Statistics for Europe, 1983 (United Nations Publication, Sales No. E.F.R.84.II.E.28)].

2. Standard vs specific calorific values

4.34. Energy products with the same chemical composition will carry the same energy content. In

practice, there are variations of the composition of the same energy product. For example, "premium"

gasoline may have slightly different chemical formulations (and therefore have a different energy

content); natural gas may contain variations in the proportions of ethane and methane; liquefied

petroleum gas (LPG) may in fact be solely propane or solely butane or any combination of the two. Only

those products which are single energy compounds, such as "pure" methane, or "pure" ethane, and

electricity (which is an energy form rather than a product) have precise and unalterable energy

contents. In addition, differences in energy content may also occur over time as the quality of the fuel

may change due, for example, to a change in the source of that fuel.

4.35. Standard calorific values refer to the energy content of fuels with specific characteristics that

are generally applicable to all circumstances (different countries, different flows, etc.). They are used

IRES

8

as default values when specific calorific values are not available. Specific calorific values, on the other

hand, are based on the specificity of the fuel in question and are measurable from the original data

source. They are particularly important for fuels which present different qualities: coal, for example,

presents a range of quality which makes it suitable for different uses. However, in using many different

specific calorific values, caution should be applied to ensure consistency between the energy content on

the supply side and on the consumption side for a same country-year.

4.36. Often there is a problem in energy statistics as the product produced may not be identical in

composition to the product in subsequent processes, even though it is referred to by the same name.

The coal extracted from a coal mine may well contain substantial quantities of waste material and be

different in chemical composition and energy content from the coal finally supplied and consumed.

Crude oil from an oil well may contain dissolved energy and non-energy gases and liquids, which are

removed from the crude oil before or when it is processed at refineries. Natural gas, whether

produced in association with crude oil or independently, may contain non-energy gases and dissolved

energy liquids that have to be separated out before natural gas of defined chemical content can be

marketed. Some of the apparent losses of energy that appear in national energy balances (and apparent

gains) could be the result of not taking into account the changes in energy content of a particular

product. In this case, flow-specific calorific values would allow for a more consistent energy balance.

4.37. An alternative to apply specific conversion factors for different flows (production, import,

export, transformation, consumption) of a same fuel is to adjust the quantities of this fuel to meet the

energy content of a grade of this fuel of a certain calorific value, constant across flows. While this

approach would make no difference in an energy balance, if compared with the previous one, it would

make the commodity balance in the original unit more consistent.

4.38. In any case, it is extremely important to provide metadata on all conversions between different

energy units undertaken to arrive at the disseminated data, in order to ensure transparency and clarity,

and to enable comparability. This would include displaying the conversion factors between original and

presented units, informing whether they are on a gross or on a net calorific basis and also detailing the

route utilized in each conversion. (base on Recommendation 25 of the UN Manual F.29 )

[Should there be a section describing how to calculate average (specific) calorific values?

We have received different views on the need for this proposed section, so we will appreciate more

feedback on the topic]

Standard calorific values for solid fuels

4.39. Since solid fuels are naturally measured by mass, Table 5 provides the standard calorific values

to convert mass/weight units of solid fuels to energy units.

Table 5: Standard solid fuel equivalents a/

Giga-joules Million

Btus

Gigacalories

Megawatt

hours

Barrels

oil eq.

Tons coal

equivalent

Tons oil

INTO equivalent

FROM

Metric tons MULTIPLY BY

Hard coal b/ 29.31 27.78 7.00 8.14 4.9 1.000 0.700

Lignite b/ 11.28 10.70 2.70 3.13 2.5 0.385 0.270

Peat 9.53 9.03 2.28 2.65 2.3 0.325 0.228

Oil shale 9.20 8.72 2.20 2.56 1.8 0.314 0.220

IRES

9

Coal briquettes 29.31 27.78 7.00 8.14 4.9 1.000 0.700

Lignite briquettes 19.64 18.61 4.69 5.45 3.3 0.670 0.469

Peat briquettes 14.65 13.89 3.50 4.07 2.5 0.500 0.350

Gas coke 26.38 25.00 6.30 7.33 4.4 0.900 0.630

Oven coke 26.38 25.00 6.30 7.33 4.4 0.900 0.630

Brown coal coke 19.64 18.61 4.69 5.45 3.4 0.670 0.469

Petroleum coke 35.17 33.33 8.40 9.77 5.9 1.200 0.840

Charcoal 28.89 27.38 6.90 8.02 4.8 0.985 0.690

Fuelwood 12.60 11.94 3.01 3.50 2.1 0.430 0.301

Source : UN Manual F.44

Note: Metric tons can be derived from units represented in the above columns by dividing by the conversion

factors in the table.

Example: Convert hard coal from GJ into metric tons. 1 GJ of hard coal = 1 / 29.31 metric ton of hard coal

a/ All heat values correspond to net calorific value.

b/ The calorific values of hard coal and lignite (or brown coal) can vary greatly by geographic or geologic

location and over time

Standard calorific values for liquid fuels

4.40. As liquid fuels are reported in mass basis, even though their original units are on a volumetric

basis (see para. 4.8), two tables are provided with standard conversion factors; one with the standard

energy contents by weight; and the other with standard densities, so that their calorific content can be

derived from either mass or volume. Table 6 presents the standard calorific values from mass units to

energy units; and Table 7 presents volume equivalents of liquid fuels from volume to mass units for a

specific gravity.

Table 6: Standard liquid fuel equivalents a/

Gigajoules

Million

Btus

Gigacalorie

Megawatt

hours

Barrels oil

eq.

Tons coal

equivalent

Tons oil

equivalent

INTO

FROM

Metric tons MULTIPLY BY

Crude oil 42.62 40.39 10.18 11.84 7.32 1.454 1.018

Nat. gas liquids 45.19 42.83 10.79 12.55 10.40 1.542 1.079

LPG/LRG 45.55 43.17 10.88 12.65 11.65 1.554 1.088

Propane 45.59 43.21 10.89 12.67 12.34 1.556 1.089

Butane 44.80 42.46 10.70 12.44 10.85 1.529 1.070

Natural gasoline 44.91 42.56 10.73 12.47 10.00 1.532 1.073

Motor gasoline 43.97 41.67 10.50 12.21 8.50 1.500 1.050

Aviation gasoline 43.97 41.67 10.50 12.21 8.62 1.500 1.050

Jet fuel gas type 43.68 41.39 10.43 12.13 8.28 1.490 1.043

Jet fuel kero. type 43.21 40.95 10.32 12.00 7.77 1.474 1.032

Kerosene 43.21 40.95 10.32 12.00 7.77 1.474 1.032

Gas-diesel oil 42.50 40.28 10.15 11.81 7.23 1.450 1.015

Residual fuel oil 41.51 39.34 9.91 11.53 6.62 1.416 0.991

Lubricating oil 42.14 39.94 10.07 11.70 6.99 1.438 1.007

Bitumen/Asphalt 41.80 39.62 9.98 11.61 6.05 1.426 0.998

Petroleum coke 36.40 34.50 8.69 10.11 5.52 1.242 0.869

Petroleum wax 43.33 41.07 10.35 12.03 7.86 1.479 1.035

Plant condensate 44.32 42.01 10.59 12.31 8.99 1.512 1.059

White spirit 43.21 40.95 10.32 12.00 7.77 1.474 1.032

IRES

10

Naphtha 44.13 41.83 10.54 12.26 8.74 1.506 1.054

Feedstocks 43.94 41.65 10.50 12.20 8.50 1.499. 1.050

Other pet. prods 42.50 40.28 10.15 11.80 6.91 1.450 1.015

Ethyl alcohol 27.63 26.19 6.60 7.68 4.60 0.94 0.660

Methyl alcohol 20.93 19.84 5.00 5.82 3.50 0.71 0.500

Source : UN Manual F.44

Note: Metric tons can be derived from the units represented in the above columns by dividing by the

conversion factors in the table.

Example: Convert metric tons of crude oil into Gigajoules: 1 metric ton of crude oil = 42.62 Gigajoules.

a/ All heat values correspond to net calorific value.

Table 7: Standard volume equivalents of liquid fuels

Litres Cubic meters US

gallons

Imperial

gallons Barrels Barrels per

day a/

INTO

FROM

Metric tons at sp. gravity MULTIPLY BY

Crude oil 0.86 1164 1.164 308 256 7.32 0.02005

Nat. gas liquids 0.55 1653 1.653 437 364 10.40 0.02849

LPG/LRG 0.54 1852 1.852 489 407 11.65 0.03192

Propane 0.51 1962 1.962 518 432 12.34 0.03381

Butane 0.58 1726 1.726 456 380 10.85 0.02974

Natural gasoline 0.63 1590 1.590 420 350 10.00 0.02740

Motor gasoline 0.74 1351 1.351 357 297 8.50 0.02329

Aviation gasoline 0.73 1370 1.370 362 301 8.62 0.02362

Jet fuel gas type 0.76 1317 1.317 348 290 8.28 0.02270

Jet fuel kero type 0.81 1235 1.235 326 272 7.77 0.02129

Kerosene 0.81 1235 1.235 326 272 7.77 0.02129

Gas-diesel oil 0.87 1149 1.149 304 253 7.23 0.01981

Residual fuel oil 0.95 1053 1.053 278 232 6.62 0.01814

Lubricating oils 0.90 1111 1.111 294 244 6.99 0.01915

Bitumen/Asphalt 1.04 962 0.962 254 212 6.05 0.01658

Petroleum coke 1.14 877 0.877 232 193 5.52 0.01512

Petroleum wax 0.80 1250 1.250 330 275 7.86 0.02153

Plant condensate 0.70 1429 1.429 378 314 8.99 0.02463

White spirit 0.81 1235 1.235 326 272 7.77 0.02129

Naphtha 0.72 1389 1.389 367 306 8.74 0.02395

Other pet. prods 0.91 1099 1.099 290 241 6.91 0.01893

Source : UN Manual F.44

Note: Metric tons can be derived from the units represented in the above columns by dividing by the

conversion factors in the table.

Example: Convert crude oil from barrels into metric tons. 1 barrel of crude oil = 1 / 7.32 metric tons of crude

oil

a/ On an annualized basis.

Standard calorific values for gaseous fuels

4.41. The original/natural unit for gaseous fuels is in volume units. Table 8 provides the standard

calorific values to convert from volume units into energy content. It should be mentioned, however, that

at international level data on gaseous fuels are generally collected from countries already in energy

units.

IRES

11

Table 8: Standard gaseous fuel equivalents a/

Gigajoules

Million

Btus

Megawatt

hours

Gigacalories

Barrels oil Tons coal

equivalent

Tons oil

equivalent

INTO

FROM

Thousand

cubic metres b/ MULTIPLY BY

Natural gas 39.02 36.98 10.84 9.32 6.50 1.331 0.932

Coke oven gas 17.59 16.67 4.88 4.20 2.94 0.600 0.420

Blast furnace gas 4.00 3.79 1.11 0.96 0.66 0.137 0.096

Refinery gas c/ 46.1 43.7 12.8 11.0 7.69 1.571 1.100

Gasworks gas 17.59 16.67 4.88 4.20 2.94 0.600 0.420

Biogas 20.0 19.0 5.6 4.8 3.36 0.686 0.480

Methane 33.5 31.7 9.30 8.0 5.59 1.143 0.800

Ethane 59.5 56.3 16.5 14.2 9.92 2.029 1.420

Propane 85.8 81.3 23.8 20.5 14.33 2.929 2.050

Isobutane 108.0 102.0 30.0 25.8 18.0 3.686 2.580

Butane 111.8 106.0 31.0 26.7 18.6 3.814 2.670

Pentane 134.0 127.0 37.2 32.0 22.36 4.571 3.200

Source : UN Manual F.44

Note: Cubic metres can be derived from the units represented in the above columns by dividing by the

conversion factors in the table. 1 cubic meter = 35.31467 cubic feet

Example: Convert natural gas from Gigajoules (GJ) into thousand m3. 1 GJ of natural gas = 1 / 39.02

thousand m3 of natural gas.

a/ All heat values correspond to net calorific value.

b/ Under standard reference conditions of 15oC, 1,013.25 mbar, dry. Adjustments may be needed under

different conditions.

c/ A factor of 0.02388 is used to convert refinery gas in terajoules to a weight basis of thousand metric tons.

Standard calorific values for electricity/heat

4.42. The original unit for electricity and heat is an energy unit (mass and volume are not applicable

units in this case). Thus there is no need for standard conversion factors for electricity and heat, but

rather a table of equivalence between energy units (e.g., GWh to TJ, TOE, Gcal, etc.), which is

presented in Table 3. A table of transformation efficiencies is not necessary either, since it is

straightforward to apply a, say, 50% efficiency to derive the energy content of entrants to a thermal

(power) plant based on its electricity or heat output.

Standard calorific values for biomass fuels

4.43. Biomass plays an important role in the energy mix of many countries. This is particularly true in

developing countries where biomass, and in particular fuelwood, is often the principal source of energy

and power in rural areas. Biomass refers to several energy sources which are typically found in the

informal sector. It includes fuelwood, charcoal, bagasse, and animal and vegetal wastes, but also to

derived biofuels such as bioethanol and biodiesel.

4.44. Fuelwood. In rural areas of many developing countries the principal source of energy for

cooking and heating is fuelwood; yet statistics on fuelwood in general are poor. This is due largely to

the fact that fuelwood is produced and traded in the informal sector.

IRES

12

4.45. Fuelwood can be measured by either volume or weight. If it is measured by volume, it can be

either stacked volume or solid volume. Measures of stacked fuelwood are the stere or stacked cubic

metre and the cord (128 stacked cubic feet). Solid volume is obtained by the water displacement

method. One advantage of measurement by volume is the relatively small influence of the moisture

content of the wood on the measurement results. The weight of fuelwood is highly dependent on

moisture content, and this is true for all biomass. The more water per unit weight, the less fuelwood.

Therefore it is important that the moisture content be accurately specified when fuelwood is measured

by weight.

4.46. There are two ways of measuring moisture content (mc). They are the so-called "dry basis" and

"wet basis" and are defined below.

Dry basis: 100

dry weight

wet weight dry weight

mc% x

−



Wet basis 100

wet weight

wet weight dry weight

mc% x

−



4.47. When biomass is very wet there is a large difference between the two moisture contents (e.g.

100 per cent mc dry basis = 50 per cent mc wet basis), but when the biomass is air-dry, the difference is

small (15 per cent mc dry basis = 13 per cent mc wet basis). It is important to state on which basis the

moisture content is measured. Most fuelwood moisture is measured on the dry basis, but some is

measured on the wet basis.

4.48. Another important determinant of the energy content of fuelwood is ash content. While the ash

content of fuelwood is generally around 1 per cent, some species can register an ash content of up to 4

per cent. This affects the energy value of the wood since the substances that form the ashes generally

have no energy value. Thus wood with 4 per cent ash content will have 3 per cent less energy content

than wood with 1 percent ash content.

4.49. The standard calorific values from mass unit to energy units provided in the UN Manual F.44

are presented in Table 9. The table shows how the calorific values vary with different moisture content

of green wood, air-dried wood and oven-dried wood.

Table 9: Influence of moisture on net calorific values of standard fuelwood

(Wood with 1 per cent ash content)

Percentage moisture

content

Kilocalories

per kilogram

Btus

per pound

Megajoules per

kilogram

dry

basis

Wet

basis

160 62 1360 2450 5.7

140 59 1530 2750 6.4

120 55 1720 3100 7.2

100 50 1960 3530 8.2

80 45 2220 4000 9.3

Green wood

70 41 2390 4300 10.0

60 38 2580 4640 10.8

50 a/ 33 a/ 2790 5030 11.7

Air-dried wood

40 29 3030 5460 12.7

IRES

13

30 23 3300 5930 13.8

25 b/ 20 b/ 3460 6230 14.5

20 17 3630 6530 15.2

15 13 3820 6880 16.0

10 9 4010 7220 16.8

5 5 4230 7610 17.7

Oven-dried wood

0 0 4470 8040 18.7

Sources: from UN Manual F.44. the original source was: Food and Agriculture Organization, A New Approach

to Domestic Fuelwood Conservation, (Rome, 1986); D. A. Tillman, Wood as an Energy Resource (New York,

Academic Press, 1978); and United Nations, Concepts and Methods for the Collection and Compilation of Statistics

on Biomass Used as Energy, by K. Openshaw (ESA/STAT/AC.3016).

a/ Average of as-received fuelwood on cordwood basis (4-foot lengths).

b/ Average of logged fuelwood.

4.50. When fuelwood is collected in volume units, a conversion factor has to be used to obtain mass

units. Table 10 shows the standard conversion factors to go from volume units to mass units. Table 11

shows how the different moisture contents of fuelwood affect the conversion factors between cubic

metres and metric tons.

Table 10: Standard fuelwood conversion table

(Wood with 20–30 per cent moisture content)

Fuel wood

Metric tons

per cubic metre

Metric tons

per cord

Cubic metres

per metric ton

Cubic feet

per metric ton

General 0.725 1.54 1.38 48.74

Coniferous 0.625 1.325 1.60 56.50

Non-Coniferous 0.750 1.59 1.33 46.97

Source: from UN Manual F.44. The original source was: Food and Agriculture Organization of the United

Nations, Yearbook of Forest Products, 1983 (Rome, 1985).

Note: 1 cord of wood = 3.624556 cubic metres = 128 cubic feet

1 stere (stacked wood) = 1 stacked m3 = 35.31467 stacked cubic feet

1 board foot of wood = 2.359737 x 10-3 m3 = 0.08333 cubic feet

Table 11: Influence of moisture on solid volume and weight of standard fuelwood

Percentage moisture content of fuelwood

100 80 60 40 20 15 12 10 0

Solid volume in m3

per ton 0.80 0.89 1.00 1.14 1.33 1.39 1.43 1.45 1.60

Weight in tons

per m3 1.25 1.12 1.00 0.88 0.75 0.72 0.70 0.69 0.63

Source: from UN Manual F.44. The original source was: Food and Agriculture Organization, Wood Fuel

Surveys, (Rome, 1983).

4.51. These tables need to be updated and revised as even the UN Manual F.44 (page 31) mentions

that

IRES

14

“Discrepancies do exist between the above two tables and this reflects much of the literature on

fuelwood measurement. It occurs in this case largely because the former is based on

information contained in standardized tables while the latter presents results of more current

research”

4.52. Charcoal. The amount of fuelwood necessary to yield a given quantity of charcoal depends

mostly on three factors: wood density, wood moisture content and the means of charcoal production.

4.53. The principal factor in determining the yield of charcoal is parent wood density, since the

weight of charcoal can vary by a factor of 2 for equal volumes. However, the moisture content of the

wood also has an appreciable effect on yields; the drier the wood, the greater is the yield. The means of

charcoal production is the third determinant of yield. Charcoal is produced in earth-covered pits, in oil

drums, in brick or steel kilns and in retorts. The less sophisticated means of production generally

involve loss of powdered charcoal (fines), incomplete carbonization of the fuelwood and combustion of

part of the charcoal product, resulting in lower yields.

4.54. There is always an amount of powdered charcoal produced in the manufacture and transport of

charcoal. If powdered charcoal undergoes briquetting, then the weight of the briquettes may be 50-100

per cent higher, per given volume of unpowdered charcoal, due to greater density.

4.55. The three variables which affect the energy value of charcoal are: moisture content, ash content

and degree of carbonization. The average moisture content of charcoal is 5 per cent. The average ash

content of wood charcoal is 4 per cent, while that of charcoal produced from woody crop residues, such

as coffee shrubs, is near 20 per cent. With the assumption of complete carbonization, the average

energy value of wood charcoal with 4 per cent ash content and 5 per cent moisture content is

approximately 30.8 MJ/kg. The average energy value of crop residue charcoal with 20 per cent ash

content and 5 per cent moisture content is 25.7 MJ/kg.

4.56. Two tables are provided pertaining to charcoal production. Table 12 illustrates the effect of

parent wood density and moisture content on charcoal yield. Table 13 supplies conversion factors for

production of charcoal by the various kilns for selected percentages of wood moisture content. It

assumes some standard hardwood as input to the process.

Table 12: Fuelwood to charcoal conversion table

Influence of parent wood density on charcoal production

(Weight (kg) of charcoal produced per cubic metre fuelwood)

Coniferous

wood

Average tropical

Hardwoods

Preferred Tropical

hardwoods

Mangrove

(rhizophora)

Charcoal 115 170 180 285

Influence of wood moisture content on charcoal production

(Quantity of wood required to produce 1 ton of charcoal)

Moisture content (dry basis) 100 80 60 40 20 15 10

Volume of wood required

(cubic metres)

17.6 16.2 13.8 10.5 8.1 6.6 5.8

Weight of wood required (tons) 12.6 11.6 9.9 7.5 5.8 4.7 4.1

Sources: from UN Manual F.44. The original source was: Wood Fuel Surveys, (Rome, 1983). D. E. Earl,

Forest Energy and Economic Development (London, Oxford University Press, 1975); and the Food and

Agriculture Organization of the United Nations.

IRES

15

Table 13: Fuelwood requirement for charcoal production by kiln type

(Cubic metres of fuelwood per ton of charcoal)

Percentage moisture content of fuelwood

Kiln Type

15 20 40 60 80 100

Earth kiln 10 13 16 21 24 27

Portable steel kiln 6 7 9 13 15 16

Brick kiln 6 6 7 10 11 12

Retort 4.5 4.5 5 7 8 9

Source: from UN Manual F.44. The original source was: Food and Agriculture Organization, Wood Fuel

Surveys, (Rome, 1983).

4.57. Vegetal and animal wastes. Energy stored in agricultural wastes and waste products from food

processing increasingly are being used to replace woody biomass in fuelwood deficient areas. These

waste products can be burned as fuels to fulfill heating or cooking requirements.

4.58. There are two important determinants of the energy value of non-woody plant biomass-one is

moisture content and the other is ash content. While the ash content of wood is generally around 1 per

cent, that of crop residues can vary from 3 per cent to over 20 per cent, and this affects the energy

value. Generally, the substances that form the ashes have no energy value. Thus biomass with 20

percent ash content will have 19 percent less energy than a similar substance with 1 per cent ash

content. Data for these potential sources of energy are rarely collected directly but derived from

crop/waste or end-product/waste ratios. Due to this wide of variability in composition, ash and moisture

content of general animal and vegetal wastes across countries, it is recommended to report these

products to international organizations in an energy unit (TJ preferably) rather than their natural units.

Country authorities in general are able to assess and determine the energy content of these wastes.

Alternatively, measuring the energy content can be accomplished by measuring the heat or electricity

output of transformation devices and applying standard efficiency factors.

4.59. Given the importance of the use of bagasse, the fibrous cane residue from the production of

sugar from sugar cane, possible estimation procedures shall be outlined for this case. Also, singling out

this specific vegetal waste allows reporting quantities to international organizations in its natural unit

(weight basis), since its composition does not allow much variation. This has been done by the

international organizations who treat bagasse separately from ordinary vegetal waste. Bagasse is used as

a fuel mostly for the sugar industry's own energy needs (at times excess electricity is also fed into the

public grid) in many sugar-producing countries. The availability of fuel bagasse can be estimated based

on either (a) data on the input of sugar cane into sugar mills, or (b) production data on centrifugal cane

sugar.

4.60. Method (a): Studies based on experiences in Central American countries, found that the yield

of fuel bagasse is approximately 280 kilograms per ton of sugar cane processed. Assuming a 50 per

cent moisture content at the time of use, 1 ton of bagasse yields 7.72 GJ. The energy values for bagasse

corresponding to 1 ton of processed sugar cane are, therefore, as follows:

2.16 GJ = 0.516 Gcal = 0.074 TCE = 0.051 TOE

4.61. Method (b): Based on observations, the Economic Commission for Latin America and the

Caribbean (ECLAC) proposed the use of 3.26 kg bagasse yield per kilogram of centrifugal sugar

IRES

16

produced. Calorific equivalents for bagasse corresponding to the production of 1 ton of sugar are as

follows:

25.2 GJ = 6 Gcal = 0.86 TCE = 0.59 TOE

4.62. Animal waste or dung is another important by-product of the agricultural sector. It can be dried

and burned directly as a fuel for space heating, cooking or crop drying. It can also be spread in the

fields as fertilizer. When used as an input to biogas digestors, the outputs are gas for cooking, heating

and lighting, and a solid residue for use as fertilizer. Table 14 presents various animal and vegetal

wastes and indicates the approximate calorific values recoverable from them when used as fuels.

Table 14: Energy values of selected animal and vegetal wastes

Wastes

Average moisture

content: dry basis

(percentage)

Approximate

ash content

(percentage)

Net calorific value

(MJ/ka)

Animal dung 15 23-27 13.6

Groundnut shells 3-10 4-14 16.7

Coffee husks 13 8-10 15.5-16.3

Bagasse 40-50 10-12 8.4-10.5

Cotton husks 5-10 3 16.7

Coconut husks 5-10 6 16.7

Rice hulls 9-11 15-20 13.8-15.1

Olives (pressed) 15-18 3 16.75

Oil-palm fibres 55 10 7.5-8.4

Oil-palm husks 55 5 7.5-8.4

Bagasse 30 10-12 12.6

Bagasse 50 10-12 8.4

Bark 15 1 11.3

Coffee husk, cherries 30 8-10 13.4

Coffee husk, cherries 60 8-10 6.7

Corncobs 15 1-2 19.3

Nut hulls 15 1-5 18.0

Rice straw & husk 15 15-20 13.4

Wheat straw & husk 15 8-9 19.1

Municipal garbage . . . . 19.7

Paper 5 1 17.6

Sawdust 50 1 11.7

Sources: from UN Manual F.44. The original source was: G. Barnard and L. Kristoferson, Agricultural

Residues as Fuel in the Third World, (London, Earth Scan, 1985); Commonwealth Science Council, Common

Accounting Procedures for Biomass Resources Assessment in Developing Countries (London, 1986); Food and

Agriculture Organization of the United Nations, Energy for World Agriculture (Rome, 1979); United States of

America, Federal Energy Administration, Energy Interrelationships (Springfield, Virginia, National Technical

Information Service, 1977).

Note: Two dots (..) indicate that data are not available.

Efficiency(ies)/useful energy

[Note this section was discussed in the F.44 manual. However, we think that it is more

appropriate and relevant to discuss this (if at all) with the context of data compilation strategies

IRES

17

and energy balances (as there is a mention to “Useful energy balance sheet”. Also, the average

efficiencies in the table refer to 1983 and need to be updated

One comment agreed to moving the section. Please provide your views.]

4.63. All processes of life require the conversion of energy from one form to another. The radiant

energy of the sun is converted by plants into stored chemical energy. Plants are then consumed by

animals and their energy is transformed into mechanical energy to move muscles and create heat. The

chemical energy stored in plants over time has also been accumulating in deposits of coal, petroleum

and natural gas which are used in devices to convert this energy into heat, mechanical and radiant

energy. Additionally, electrical energy can be produced from mechanical energy so that energy may be

transported over long distances and then utilized by the appliances of the final consumers.

4.64. When assessing energy transformation/conversion devices, it is desirable to measure the energy

input and output, from which one can derive the device’s conversion efficiency and have a more

accurate picture of the energy flows. However, when only energy input or energy output is available,

standard efficient coefficients of similar devices could be used to estimating the missing variable

(output in the first case, and input in the second).

4.65. The concept of useful energy tries to gauge how much of the energy content of the consumed

product is not wasted, but rather is working for the end-use it is intended for. Unlike in the assessment

of transformation devices, in surveying final-use appliances it is mostly impracticable to measure the

useful energy output, particularly in households (e.g. the light emitted by an incandescent bulb, as

opposed to the generated heat; or the useful heat generated by a residential boiler burning gas or fuel

oil). In some cases, it is also difficult to measure the energy input individually (what percentage of the

total electricity consumption of a household goes to lighting, for example). In this case, standard

efficiencies, together with assessment of time-use of individual appliances in household surveys, can

provide a picture of the useful energy by end-use. The measurement of useful energy requires that the

following be recorded:

(a)The main types of appliances used by final energy consumers;

(b)The amount of energy actually used by these various appliances, or an estimate based on their

utilization (time x average power input);

(c)The average efficiencies of these appliances when in normal use.

4.66. Table 15 examines present the average efficiencies of different devices and appliances. “Useful

energy balance-sheets” [these should be explained], in addition to recording other losses, take account

of the transformation of energy in the appliances of the final consumer.

Table 15: Average efficiencies of appliances at the final consumption stage

Appliances Percentage

Three stone wood fire

Charcoal stove

10 – 15

20 – 30

Cement kilns

Glassworks radiation furnace

Blast furnace

30 – 40

40

70 – 77

Gas engine

Diesel engine

Jet engine

22

35

25

IRES

18

Coal-fired industrial furnaces and boilers

Coal-fired cooker

Coal-fired domestic heating boiler and coal - fired stove

60

25

55 – 65

Oil-fired industrial furnaces and boilers

Oil-fired domestic heating boiler

District heating boilers fired with residual fuel oil

68 – 73

68 – 73

66 – 73

Parafin burners 55

Gas-fired industrial furnaces and boilers .

Gas cooker

Gas-fired water heater

Gas-fired domestic heating boiler

70 – 75

37

62

67 – 80

LPG cooker

Space heating with LPG

37

69 – 73

Electric motors

Electric furnaces

Electrolysis

Electric rail haulage

Electric cooker

Electric water heater

Direct electric heating

Incandescent electric lighting

Fluorescent electric lighting

95

95

30

90

75

90

100

6

20

Sources: from UN Manual F.44. The original source was: European Economic Community, Statistical

Office of the European Communities (EUROSTAT), Useful Energy Balance Sheets, Supplement to Energy

Statistics Yearbook (Brussels, 1983); and United Nations, "Concepts and methods for the collection and

compilation of statistics on biomass used as energy", by K. Openshaw (ESA/STAT/AC.30/6).

4.67. Employing these, the useful energy balance-sheet is able to present a fifth category of energy

losses - those at the final consumer stage. Thus, from primary input to final consumer offtake, the

losses recorded are:

(a)Losses in the primary production/extraction process (gas flared, coal fines lost, etc.);

(b)Transformation losses from primary to secondary sources of energy;

(c)Distribution losses which largely affect gaseous fuels and electricity;

(d)Consumption by the energy sector for plant operations;

(e)Losses at the final consumer stage due to the operating efficiencies of the appliances which

transform the energy for the last time.

D. Recommendations

[TO BE DISCUSSED]

The recommendations on “accounting units and conversion” in the UN Manual F.29 are the following (

they are taken verbatim and are presented here so that they can be reviewed and amended as needed).

(Rec. 25) Energy balances should contain in the column headings for each energy source the

average conversion factor (appropriate for expressing the original units in (or underlying) that

column in terms of the common accounting unit as shown in the balance). Such average factors

should be complemented in foot-notes, or accompanying text; with clear descriptions of the

IRES

19

routes and stages followed in any conversions that are not adequately defined by the average

factors (para. 268).

(Rec. 5) National and international statistical offices, and bodies that advise them or undertake

work for them, should always define clearly the accounting units or presentation units employed

in published analyses. The conversion factors and the route used to convert original physical

units into the chosen common accounting unit or units should also be stated, or readily available

published sources where they may be found should be cited. It should also be made clear

whether energy units are defined on a gross or net calorific basis (para.48; see also (19) and

(20), below).

(19) When expressing the energy content of primary and secondary fossil energy sources in terms of

a common energy accounting unit, net calorific values (NCV) should be used in preference to

gross calorific values (GCV). If and when recuperation of a significant part of the difference

between GCV and NCV from exhaust gases becomes a practical possibility and seems likely to

become a reality, this recommended basis may need to be reconsidered (para. 135).

(20) Given that the joule, and multiples of it by raising it to powers of 103, is the only energy unit in

the SI, international and national statistical offices should consider adopting the joule (1 joule =

0.239 calorie) as the rigorous accounting unit for energy balances. The TOE (1 TOE = 107 kcal

NCV) and/or TCE (l TCE= 7 x 106 kcal NCV) may be used as supplementary presentation

units. Whenever they are used, they should be clearly defined in terms of the joule, and the

route used for converting original data to TOE or TCE should be clearly described (para. 157).

[THE FOLLOWING MAY BE RECOMMENDED – FOR DISCUSSION]

4.68. It is recommended that for international reporting, and as far as possible in national accounting

procedures, energy statisticians should use the International System of Units, officially abbreviated SI.

4.69. It is recommended to collect data in original and common units and on the specific conversion

factors used in the conversion to the common units. Standard calorific values are to be used in absence

of specific conversion factors.

4.70. The units to be recommended for data collection [can this be recommended? If so, only to

international data compilation or also to national statistics data collection and/or dissemination?

For all products or might there be exceptions (e.g., waste)? We have received different views on

the subject as a general question, and the Cslo Group is invited to provide further comments on

the specifics; whether this can be recommended and for which fuels] for each class of fuels are as

displayed on Table 16. Where there is no mention, it applies to primary as well as derived fuels.

Table 16: Recommended(?) measurement units

Dimension Unit

Solid fossil fuels Mass Thousand tons

Liquid fuels (fossil and biofuels) Mass Thousand tons

Gases Energy Terajoules

Wastes Energy Terajoules

Fuelwood Volume Thousand cubic metres

Charcoal Mass Thousand tons

Electricity energy (power x time) GWh

Electricity installed capacity Power MW

Refinery capacity mass/time Thousand tons/year

IRES

20

Heat Energy Terajoules

4.71. When the type of waste is well-defined in its constitution, rather than only by the process by

which it was generated, one can assume that there should not be great variation in specific conversion

factors. In this case, data can be reported on a weight basis (thousand metric tons). Even so, if the

specific conversion factors are available, they should be provided. Bagasse and black liquor (also

referred to as pulp and paper waste) both fall in such case.

4.72. Common units. One TCE has traditionally been defined as comprising 7 x 106 kcal and one

TOE as l x 107 kcal. The conversion from original units into TCE or TOE implies choosing coefficients

of equivalence between different forms and sources of primary energy. When using TCE and TOE as

common unit (or any other unit based on one particular fuel for the same effect), it should not be

assumed that one ton of coal has one TCE or that one ton of oil has one TOE of energy content. This

approach could lead to distortions since there is a wide spread in calorific values among types of coal

and individual petroleum products, and between calorific values of coals and crude oils in different

countries. Rather, it is recommended first to convert data to an energy unit (terajoules, for example),

using the pertinent conversion factors, and then from this energy unit directly to TCE or TOE. This

approach entails, for example, having different conversions factors for each grade of coal and treating

them separately.

[Do we need to give guidance on the conversion of toe and TCE to Tj? The consideration here is

that country practices might define the toe or the TCE differently]

4.73. Net and Gross calorific values. Net (rather than gross) calorific values (NCVs rather than

GCVs) should be applied. In other words, the heat required to evaporate moisture, which is present in all

fuels (except electricity) and is also produced in the combustion process, should not be treated as part

of a fuel's energy providing capability

[The standard default conversion factors should be updated. The text below is from the

presentation on net/gross calorific values at the 3rd OG meeting]

It would be helpful if countries that are recuperating the latent heat in CHP plants provide information

on this process, including estimates of what proportion of total energy consumption is represented. [Is it

feasible to provide this proportion? Please provide comments]

For now, technological advances have not gone far enough to justify changing from GCVs to NCVs for

the balances.

The default gross/net ratios and fuel equivalents should be evaluated systematically (using “real”

measurements) and probably updated.

We recommend that experts proceed with a campaign of tests and measurements in as many countries

as possible. Analysis should be undertaken to determine whether region-specific NCVs are useful.

Comparison of solid fuel equivalents between organisations (GJ/t)

UN IEA defaults

defaults

IPCC defaults

(2006 GLs)

Old Europe N. Amer. Pacific

Hard Coal 29.31 25.8-28.2 country-specific

Lignite 11.28 11.9 country-specific

Peat 9.53 9.76 8.374 9.76

IRES

21

# Comments

This chapter has a plethora of tabulations.  This is not suitable for a chapter in IRES.  These tables should be in an Annex and referred to from this chapter.  This chapter should focus on the principles of measurement units and conversion factors (which I will leave to others), without the distraction of all these tables.

Can’t this be derived from Table 5?

I didn’t think there was a clear consensus on moving to NCV during OG4.  Many countries still use GCV, and it would be difficult to get these countries to agree to such a recommendation.