# Measurement units and conversion factors

Pending questions for the members of the Oslo Group:

- Should the tables for standard/default calorific values be updated?

  - If so, which source to use (c.f., Karen Treanton’s presentation)?

- Table 11 (% difference between GCVs and NCVs): Should it be updated?

  - If so, which source to use? Some of the values can be derived from the IEA/Eurostat manual.

- Should a small Section exist on how to calculate country-specific conversion factors?

  - Leonardo from UNSD will propose some text during the VM1.

- Is “Default calorific values” a better name than “Standard calorific values”?

  - The concern is that the word “standard” might imply it is the standard to use, rather than a proxy value to use in the absence of precise information.

- Review recommendations for modification/insertion/deletion

- Please indicate if any table is deemed unnecessary.

- Glossary: is it useful? Should it be expanded (if so, please provide additional entries with respective descriptions)? Please review it.

- Any suggestion for Box 4.1?

- Should the subsection on biomass (“Standard calorific values for biomass fuels” on Section C) be shortened, having the bulk of it moved to ESCM?

  - If so, please suggest what should be moved.

## Introduction

Energy products are measured in physical units by their weight or mass, volume, and energy.  The measurement units that are specific to an energy product and are employed at the point of measurement of the energy flow are often referred to as “original” or “natural” units (IEA/Eurostat Manual page 19).  Coal, for example, is generally measured by its mass or weight and crude oil by its volume.  In cross-fuel tabulations such as the energy balances energy sources and commodities are also displayed in a “common unit” to allow comparison across sources.  These “common” units are usually energy units and require the conversion of a quantity of a product from its original units through the application of an appropriate conversion factor.

When different units are used to measure a product, the compiler is left with the task of converting units which, in absence of specific information on the products (such as density, gravity and calorific value), may lead to different figures.

This chapter provides a review of the physical measurement units used for energy statistics, explains the concepts of original and common units, discusses the importance of conversion factors for the conversion from original to common units and presents standard conversion factors to use in absence of country- or region-specific conversion factors.

## Measurement units

This section covers the “original” or “natural” units as well as the common units.  It also makes reference to the International System of Units – often abbreviated as SI from the French “Système International d’Unités” – which is a modernized version of the metric system established by international agreement.  It provides a logical and interconnected framework for all measurements in science, industry and commerce.  The SI is built upon a foundation of seven base units plus two supplementary units.  Multiples and sub-multiples are expressed in the decimal system. See Box 4.1for more details on SI.

Standardization in the recording and presentation of original units is a primary task of an energy statistician before quantities can be analyzed or compared. (UN Manual F.44 page 11).

Box 4.1: International System of Units

### Original units

As mentioned in para 4.1, original units are the units of measurement employed at the point of measurement of the product flow that are those best suited to its physical state (solid, liquid or gas) and that require the simplest measuring instruments (IEA/Eurostat Manual page 19).  Typical examples are mass units (e.g. kilograms or tons) for solid fuels, volume units (e.g. barrels or litres) or weight units (tons) for oil and volume units (e.g. cubic metres) for gases.  The actual units used nationally vary according to country and local condition and reflect historical practice in the country, sometimes adapted to changing fuel supply conditions (IEA/Eurostat Manual page 177).

Electricity is measured in kilowatt-hour (kWh), an energy unit (although it is rather a unit of work) which allows one to perceive the electrical energy in terms of the time an appliance of a specified wattage takes to “consume” this energy. Heat quantities in steam flows are calculated from measurements of the pressure and temperature of the steam and may be expressed in calories or joules. Apart from the measurements to derive the heat content of steam, heat flows are rarely measured but inferred from the fuel used to produce them.

It should be noted that it may occur that, in questionnaires for the collection of energy statistics, data may be required to be reported in different units from the original/natural unit. For example, statistics on crude oil and oil products may be requested in a mass or weight basis since the heating value of oil products by weight displays less variation than the heating value by volume. Statistics on gases, as well as wastes, can be requested in terajoules or other energy unit in order to ensure comparability, since gases (and wastes) are usually defined on the basis of their production processes, rather than their chemical composition and different compositions of the same type of gas (or waste) entail different energy contents by volume. Collection of statistics on wastes in an energy unit is based on the measured or inferred heat output, as in energy statistics waste refers only to the portion used directly for heat raising.

#### Mass units

Solid fuels, such as coal and coke, are generally measured in mass units.  The SI unit for mass is the kilograms (kg).  Metric tons (tons) are most commonly used - for example, to measure coal and their derivatives. One ton corresponds to 1000 kg. Other units of mass used by countries include: pound (0.4536 kg), short ton (907.185 kg) and long ton (1016.05 kg).  Table 8 in the Annex presents the equivalent factors to convert different mass units.

#### Volume units

Volume units are original units for most liquid and gaseous, as well as for some traditional fuels.  The SI unit for volume is the cubic metre which is equivalent to a kilolitre or one thousand litres.  Other volume units include: the British or Imperial gallon (4.546 litres), United States gallon (3.785 litres), the barrel (159 litres) and the cubic feet, which is also used to measure volumes of gaseous fuels.  Given the preference from oil markets for the barrel as a volume unit, the barrel per day is commonly used within the petroleum sector so as to allow direct data comparison across different time frequencies (e.g., monthly versus annual crude oil production). However, in principle other units of volume per time can be used for the same purpose.  Table 9 in the Annex shows the equivalent factors to convert volume units.

#### Conversions between mass and volume - Specific gravity and density

Since liquid fuels can be measured by either weight or volume it is essential to be able to convert one into the other.  This is accomplished by using the density of the liquid.  Specific gravity is the ratio of the mass of a given volume of oil at 15°C to the mass of the same volume of water at that temperature.  Density is the mass per unit volume.

| Specific gravity= | Mass oil |  | Density= | mass |
| --- | --- | --- | --- | --- |
|  | mass water |  |  | volume |

When density is expressed in kilograms per litre, it is equivalent to the specific gravity.  When using the SI or metric system, in order to calculate volume, mass is divided by the specific gravity or density. Vice versa, to obtain mass, volume is multiplied by the specific gravity or density.  When using other measurement systems, one must consult tables of conversion factors to move between mass and volume measurements.

Another measure to express the gravity or density of liquid fuels is API gravity, a standard adopted by the American Petroleum Institute.  API gravity is related to specific gravity by the following formula:

| API gravity = | 141.5 | - 131.5 |
| --- | --- | --- |
|  | specific gravity |  |

Thus specific gravity and API gravity are inversely related.  They are both useful in that specific gravity increases with energy content per unit volume (e.g. barrel), while API gravity increases with energy content per unit mass (e.g. ton).

#### Energy units

Energy, heat, work and power are four concepts that are often confused. If force is exerted on an object and moves it over a distance, work is done, heat is released (under anything other than unrealistically ideal conditions) and energy is transformed.  Energy, heat and work are three facets of the same concept.  Energy is the capacity to do (and often the result of doing) work.  Heat can be a by-product of work, but is also a form of energy.  For example, in an automobile with a full tank of gasoline, embodied in that gasoline is chemical energy with the ability to create heat (with the application of a spark) and to do work (the gasoline combustion powers the automobile over a distance).

The SI unit of energy, heat and work is the joule (J).  Other units include: the kilogram calorie in the metric system, or kilocalorie, (kcal) or one of its multiples; the British thermal unit (Btu) or one of its multiples; and the kilowatt hour (kWh).

Power is the rate at which work is done (or heat released, or energy converted).  A given light bulb draws 100 joules of energy per second of electricity, and uses that electricity to emit light and heat (both forms of energy).  The rate of one joule per second is called a watt.  The light bulb, operating at 100 J/s, is drawing power of 100 Watts.

The joule is a precise measure of energy and work.  It is defined as the work done when a constant force of 1 Newton is exerted on a body with mass of 1 gram to move it a distance of 1 metre.  One joule of heat is approximately equal to one fourth of a calorie and one thousandth of a Btu.  Common multiples of the joule are the megajoule, gigajoule, terajoule and petajoule.

The gram calorie is a precise measure of heat energy and is equal to the amount of heat required to raise the temperature of 1 gram of water at 14.5(C by 1 degree Celsius.  It may also be referred to as an International Steam Table calorie (IT calorie).  The kilocalorie and the teracalorie are its two multiples which find common usage in the measurement of energy commodities.

The British thermal unit is a precise measure of heat and is equal to the amount of heat required to raise the temperature of 1 pound of water at 60°F by 1 degree Fahrenheit.  Its most used multiples are the therm (105 Btu) and the quad (1015 Btu).

The kilowatt hour is a precise measure of heat and work.  It is the work equivalent to 1000 watts (joules per second) over a one hour period. Thus 1 kilowatt-hour equals 3.6x106 joules.  Electricity is generally measured in kilowatt hour.

### Common units

As mentioned before, the original units in which energy sources and commodities are most naturally measured vary (e.g. tons, barrels, kilowatt hours, therm, calories, joules, cubic metres), thus quantity of energy sources and commodities are generally converted into a common unit to allow, for example, comparisons of fuel quantities and estimate efficiencies.  The conversion from different units to a common unit requires some conversion factors for each product.

The energy unit in the International System of Units is the joule which is very commonly used in energy statistics as a common unit.  Other energy units are also used such as: the ton of oil equivalent (toe) (41.868 gigajoules), the gigawatt-hour (GWh), the British thermal unit (Btu) (1055.1 joules) and its derived units – therm (1015 Btu) and quad (105 Btu) - and the teracalorie (4.205 joules).

In the past, when coal was the principal commercial fuel, the ton of coal equivalent (tce) was commonly used.  However, with the increasing importance of oil, it has been replaced by the ton of oil equivalent.  Table 10 in Annex shows the conversion equivalents between the common units.

## Calorific values

[the standard factors displayed in the tables are from the UN manual F. 44.  They need to be reviewed and discussed]

Calorific value or heating value of a fuel express the heat obtained from one unit of the fuel. They are necessary for the compilation of overall energy balances, to convert from the original units in which the fuels are measured to a common unit of measurement. In addition, it may also be necessary to apply some form of conversion for certain individual fuels (e.g. to express different grades of coal in terms of coal of a standard calorific content). Even though calorific values are often considered in the context of the preparation of energy balances, they have wider application in the preparation of any tables designed to show energy in an aggregated form or in the preparation of inter-fuel comparative analyses.

Calorific values are obtained by measurements in a laboratory specializing in fuel quality determination. They should preferably be in terms of joules (or any of its multiples) per original unit, for example gigajoule/ton (GJ/t) or gigajoule/cubic metre (GJ/m3). Major fuel producers (mining companies, refineries, etc.) measure the calorific value and other qualities of the fuels they produce. A calorific value is a conversion factor, in the sense that it can be used to convert mass or volume quantities into energy content.

There are two main issues as regards calorific values: the first one refers to whether they are measured gross or net of the heat necessary to evaporate the water formed during combustion and the water previously present in the fuel in the form of moisture; and the second one is related to the quality of the energy product, as the calorific value of, say, a ton of hard coal may vary greatly by geographic and geological location. These two issues are discussed in detail in the next two sections.

### Gross and net calorific/ heating values

The expression of original units of energy sources in terms of a common unit may be made on two bases as the energy stored in fuels may be measured in two stages.  The gross calorific value (GCV), or high heat value, measures the total (maximum) amount of heat that is produced by combustion.  However, part of this heat will be locked up in the latent heat of evaporation of any water present in the fuel before combustion (moisture) or generated in the combustion process.  This latter comes from the combination of hydrogen present in the fuel with the oxidant oxygen (O2) present in the air to form H2O.  This combination itself releases heat, but this heat is partly used in the evaporation of the generated water.

The net calorific value (NCV), or low heat value, excludes this latent heat. NCV is that amount of heat which is actually available from the combustion process for capture and use. The higher the moisture of a fuel or its hydrogen content, the greater is the difference between GCV and NCV. For some fuels with very little or no hydrogen content (e.g., some types of coke, blast furnace gas), this difference is negligible. In terms of magnitude, the difference between gross and net calorific values of commercial energy sources (coal, oil, products, and gas) is less than 10 per cent while that of traditional energy (fuelwood, bagasse) is usually more than 10 per cent.  Figures for the main energy commodities are presented in the Annex in Table 11.The applied technology to burn a fuel can also play a role in determining the NCV of the fuel, depending for example on how much of the latent heat it can recover from the exhaust gases.

NCVs are to be preferred over GCVs when building a balance, since most current technologies are still not able to recover the latent heat, which would thus not be treated as part of a fuel's energy providing capability. However, providing both gross and net calorific values while making clear which one (preferably net) is used in the balance is a good practice that should be encouraged, in order to allow monitoring technological advances in respect to recovering latent heat. (c.f. § 133, 135, UN Manual F.29)

### Standard vs specific calorific values

Energy products with the same chemical composition will carry the same energy content.  In practice, there are variations of the composition of the same energy product.  For example, "premium" gasoline may have slightly different chemical formulations (and therefore have a different energy content); natural gas may contain variations in the proportions of ethane and methane; liquefied petroleum gas (LPG) may in fact be solely propane or solely butane or any combination of the two.  Only those products which are single energy compounds, such as "pure" methane, or "pure" ethane, and electricity (which strictly speaking is an energy form rather than a product) have precise and unalterable energy contents.  In addition, differences in energy content may also occur over time as the quality of the fuel may change due, for example, to a change in the source of that fuel.

Standard calorific values refer to the energy content of fuels with specific characteristics that are generally applicable to all circumstances (different countries, different flows, etc.).  They are used as default values when specific calorific values are not available. Specific calorific values, on the other hand, are based on the specificity of the fuel in question and are measurable from the original data source.  They are particularly important for fuels which present different qualities: coal, for example, displays a range of quality which makes it suitable for different uses. The respective calorific values are thus specific to the fuel and flow in question. However, in using many different specific calorific values, caution should be applied to ensure consistency between the energy content on the supply side and on the consumption side for a same country-year.

Often there is a problem in energy statistics as the product produced may not be identical in composition to the product in subsequent processes, even though it is referred to by the same name.  Natural gas can be enriched with oil products, for example, to meet market specifications. Motor gasoline can be blended with ethanol and sold as motor gasoline; and depending on the country practice, this may be recorded as consumption of only motor gasoline. In this case, flow-specific calorific values would allow for a more consistent energy balance.

An alternative to apply specific conversion factors for different flows (production, import, export, transformation, consumption) of a same fuel is to adjust the quantities of this fuel to meet the energy content of a grade of this fuel of a certain calorific value, constant across flows.  While this approach would make no difference in an overall energy balance, if compared with the previous one, it would make the commodity balance in the original unit more consistent with the overall balance in energy units.

In any case, it is recommended to provide metadata on all conversions between different energy units undertaken to arrive at the disseminated data, in order to ensure transparency and clarity, and to enable comparability. This would include displaying the conversion factors between original and presented units, informing whether they are on a gross or on a net calorific basis and also detailing the route utilized in each conversion. (based on Recommendation 25 of the UN Manual F.29).

Efforts should be made to arrive at country-specific calorific values in the case they are not already available, and use of the standard factors should be encouraged only as a last resource.

[TO INSERT A SECTION ON HOW TO CALCULATE SPECIFIC CALORIFIC VALUES]

#### Standard calorific values for solid fuels

Since solid fuels are naturally measured by mass, Table 1 provides the standard calorific values to convert mass/weight units of solid fuels to energy units.

Table 1: Standard solid fuel equivalents  a/

| INTO FROM Metric tons | Giga-joules | Million Btus | Giga-calories | Megawatt hours | Barrels oil eq. | Tons coal equivalent | Tons oil equivalent |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | MULTIPLY BY |
| Hard coal b/ | 29.31 | 27.78 | 7.00 | 8.14 | 4.9 | 1.000 | 0.700 |
| Lignite b/ | 11.28 | 10.70 | 2.70 | 3.13 | 2.5 | 0.385 | 0.270 |
| Peat | 9.53 | 9.03 | 2.28 | 2.65 | 2.3 | 0.325 | 0.228 |
| Oil shale | 9.20 | 8.72 | 2.20 | 2.56 | 1.8 | 0.314 | 0.220 |
| Coal briquettes | 29.31 | 27.78 | 7.00 | 8.14 | 4.9 | 1.000 | 0.700 |
| Lignite briquettes | 19.64 | 18.61 | 4.69 | 5.45 | 3.3 | 0.670 | 0.469 |
| Peat briquettes | 14.65 | 13.89 | 3.50 | 4.07 | 2.5 | 0.500 | 0.350 |
| Gas coke | 26.38 | 25.00 | 6.30 | 7.33 | 4.4 | 0.900 | 0.630 |
| Oven coke | 26.38 | 25.00 | 6.30 | 7.33 | 4.4 | 0.900 | 0.630 |
| Brown coal coke | 19.64 | 18.61 | 4.69 | 5.45 | 3.4 | 0.670 | 0.469 |
| Petroleum coke | 35.17 | 33.33 | 8.40 | 9.77 | 5.9 | 1.200 | 0.840 |
| Charcoal | 28.89 | 27.38 | 6.90 | 8.02 | 4.8 | 0.985 | 0.690 |
| Fuelwood | 12.60 | 11.94 | 3.01 | 3.50 | 2.1 | 0.430 | 0.301 |

Source : UN Manual F.44

Note:  Metric tons can be derived from units represented in the above columns by dividing by the conversion factors in the table.

Example:  Convert hard coal from GJ into metric tons.    1 GJ of hard coal = 1 / 29.31 metric ton of hard coal

a/  All heat values correspond to net calorific value.

b/  The calorific values of hard coal and lignite (or brown coal) can vary greatly by geographic or geologic location and over time

#### Standard calorific values for liquid fuels

As liquid fuels are reported on a mass basis, even though their original units are on a volumetric basis (see para. 4.8), two tables are provided with standard conversion factors; one with the standard energy contents by weight; and the other with standard densities, so that their calorific content can be derived from either mass or volume.  Table 2 presents the standard calorific values from mass units to energy units; and Table 3 presents volume equivalents of liquid fuels from volume to mass units for a specific gravity.

Table 2: Standard liquid fuel equivalents  a/

| INTO FROM Metric tons | Giga- joules | Million Btus | Giga-calorie | Megawatt hours | Barrels oil eq. | Tons coal equivalent | Tons oil equivalent |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | MULTIPLY BY |
| Crude oil | 42.62 | 40.39 | 10.18 | 11.84 | 7.32 | 1.454 | 1.018 |
| Nat. gas liquids | 45.19 | 42.83 | 10.79 | 12.55 | 10.40 | 1.542 | 1.079 |
| LPG/LRG | 45.55 | 43.17 | 10.88 | 12.65 | 11.65 | 1.554 | 1.088 |
| Propane | 45.59 | 43.21 | 10.89 | 12.67 | 12.34 | 1.556 | 1.089 |
| Butane | 44.80 | 42.46 | 10.70 | 12.44 | 10.85 | 1.529 | 1.070 |
| Natural gasoline | 44.91 | 42.56 | 10.73 | 12.47 | 10.00 | 1.532 | 1.073 |
| Motor gasoline | 43.97 | 41.67 | 10.50 | 12.21 | 8.50 | 1.500 | 1.050 |
| Aviation gasoline | 43.97 | 41.67 | 10.50 | 12.21 | 8.62 | 1.500 | 1.050 |
| Jet fuel gas type | 43.68 | 41.39 | 10.43 | 12.13 | 8.28 | 1.490 | 1.043 |
| Jet fuel kero. type | 43.21 | 40.95 | 10.32 | 12.00 | 7.77 | 1.474 | 1.032 |
| Kerosene | 43.21 | 40.95 | 10.32 | 12.00 | 7.77 | 1.474 | 1.032 |
| Gas-diesel oil | 42.50 | 40.28 | 10.15 | 11.81 | 7.23 | 1.450 | 1.015 |
| Residual fuel oil | 41.51 | 39.34 | 9.91 | 11.53 | 6.62 | 1.416 | 0.991 |
| Lubricating oil | 42.14 | 39.94 | 10.07 | 11.70 | 6.99 | 1.438 | 1.007 |
| Bitumen/Asphalt | 41.80 | 39.62 | 9.98 | 11.61 | 6.05 | 1.426 | 0.998 |
| Petroleum coke | 36.40 | 34.50 | 8.69 | 10.11 | 5.52 | 1.242 | 0.869 |
| Petroleum wax | 43.33 | 41.07 | 10.35 | 12.03 | 7.86 | 1.479 | 1.035 |
| Plant condensate | 44.32 | 42.01 | 10.59 | 12.31 | 8.99 | 1.512 | 1.059 |
| White spirit | 43.21 | 40.95 | 10.32 | 12.00 | 7.77 | 1.474 | 1.032 |
| Naphtha | 44.13 | 41.83 | 10.54 | 12.26 | 8.74 | 1.506 | 1.054 |
| Feedstocks | 43.94 | 41.65 | 10.50 | 12.20 | 8.50 | 1.499. | 1.050 |
| Other pet. prods | 42.50 | 40.28 | 10.15 | 11.80 | 6.91 | 1.450 | 1.015 |
| Ethyl alcohol | 27.63 | 26.19 | 6.60 | 7.68 | 4.60 | 0.94 | 0.660 |
| Methyl alcohol | 20.93 | 19.84 | 5.00 | 5.82 | 3.50 | 0.71 | 0.500 |

Source : UN Manual F.44

Note:  Metric tons can be derived from the units represented in the above columns by dividing by the conversion factors in the table.

Example:  Convert metric tons of crude oil into Gigajoules:    1 metric ton of crude oil = 42.62 Gigajoules.

a/ 	All heat values correspond to net calorific value.

Table 3: Standard volume equivalents of liquid fuels

| INTO FROM Metric tons at sp. gravity | Litres | Cubic meters | US gallons | Imperial gallons | Barrels | Barrels per day a/ |
| --- | --- | --- | --- | --- | --- | --- |
|  | MULTIPLY BY |
| Crude oil | 0.86 | 1164 | 1.164 | 308 | 256 | 7.32 | 0.02005 |
| Nat. gas liquids | 0.55 | 1653 | 1.653 | 437 | 364 | 10.40 | 0.02849 |
| LPG/LRG | 0.54 | 1852 | 1.852 | 489 | 407 | 11.65 | 0.03192 |
| Propane | 0.51 | 1962 | 1.962 | 518 | 432 | 12.34 | 0.03381 |
| Butane | 0.58 | 1726 | 1.726 | 456 | 380 | 10.85 | 0.02974 |
| Natural gasoline | 0.63 | 1590 | 1.590 | 420 | 350 | 10.00 | 0.02740 |
| Motor gasoline | 0.74 | 1351 | 1.351 | 357 | 297 | 8.50 | 0.02329 |
| Aviation gasoline | 0.73 | 1370 | 1.370 | 362 | 301 | 8.62 | 0.02362 |
| Jet fuel gas type | 0.76 | 1317 | 1.317 | 348 | 290 | 8.28 | 0.02270 |
| Jet fuel kero type | 0.81 | 1235 | 1.235 | 326 | 272 | 7.77 | 0.02129 |
| Kerosene | 0.81 | 1235 | 1.235 | 326 | 272 | 7.77 | 0.02129 |
| Gas-diesel oil | 0.87 | 1149 | 1.149 | 304 | 253 | 7.23 | 0.01981 |
| Residual fuel oil | 0.95 | 1053 | 1.053 | 278 | 232 | 6.62 | 0.01814 |
| Lubricating oils | 0.90 | 1111 | 1.111 | 294 | 244 | 6.99 | 0.01915 |
| Bitumen/Asphalt | 1.04 | 962 | 0.962 | 254 | 212 | 6.05 | 0.01658 |
| Petroleum coke | 1.14 | 877 | 0.877 | 232 | 193 | 5.52 | 0.01512 |
| Petroleum wax | 0.80 | 1250 | 1.250 | 330 | 275 | 7.86 | 0.02153 |
| Plant condensate | 0.70 | 1429 | 1.429 | 378 | 314 | 8.99 | 0.02463 |
| White spirit | 0.81 | 1235 | 1.235 | 326 | 272 | 7.77 | 0.02129 |
| Naphtha | 0.72 | 1389 | 1.389 | 367 | 306 | 8.74 | 0.02395 |
| Other pet. prods | 0.91 | 1099 | 1.099 | 290 | 241 | 6.91 | 0.01893 |

Source : UN Manual F.44

Note:  Metric tons can be derived from the units represented in the above columns by dividing by the conversion factors in the table.

Example:  Convert crude oil from barrels into metric tons.   1 barrel of crude oil = 1 / 7.32 metric tons of crude oil

a/ 	On an annualized basis.

#### Standard calorific values for gaseous fuels

The original/natural unit for gaseous fuels is in volume units. Table 4 provides the standard calorific values to convert from volume units into energy content. It should be mentioned, however, that at international level data on gaseous fuels are generally collected from countries already in energy units.

Table 4: Standard gaseous fuel equivalents  a/

| INTO FROM Thousand cubic metres b/ | Giga- joules | Million Btus | Megawatt hours | Giga-calories | Barrels oil | Tons coal equivalent | Tons oil equivalent |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | MULTIPLY BY |
| Natural gas | 39.02 | 36.98 | 10.84 | 9.32 | 6.50 | 1.331 | 0.932 |
| Coke oven gas | 17.59 | 16.67 | 4.88 | 4.20 | 2.94 | 0.600 | 0.420 |
| Blast furnace gas | 4.00 | 3.79 | 1.11 | 0.96 | 0.66 | 0.137 | 0.096 |
| Refinery gas c/ | 46.1 | 43.7 | 12.8 | 11.0 | 7.69 | 1.571 | 1.100 |
| Gasworks gas | 17.59 | 16.67 | 4.88 | 4.20 | 2.94 | 0.600 | 0.420 |
| Biogas | 20.0 | 19.0 | 5.6 | 4.8 | 3.36 | 0.686 | 0.480 |
| Methane | 33.5 | 31.7 | 9.30 | 8.0 | 5.59 | 1.143 | 0.800 |
| Ethane | 59.5 | 56.3 | 16.5 | 14.2 | 9.92 | 2.029 | 1.420 |
| Propane | 85.8 | 81.3 | 23.8 | 20.5 | 14.33 | 2.929 | 2.050 |
| Isobutane | 108.0 | 102.0 | 30.0 | 25.8 | 18.0 | 3.686 | 2.580 |
| Butane | 111.8 | 106.0 | 31.0 | 26.7 | 18.6 | 3.814 | 2.670 |
| Pentane | 134.0 | 127.0 | 37.2 | 32.0 | 22.36 | 4.571 | 3.200 |

Source : UN Manual F.44

Note:  Cubic metres can be derived from the units represented in the above columns by dividing by the conversion factors in the table.     1 cubic meter  =  35.31467 cubic feet

Example:  Convert natural gas from Gigajoules (GJ) into thousand m3.     1 GJ of natural gas = 1 / 39.02 thousand m3 of natural gas.

a/ All heat values correspond to net calorific value.

b/ Under standard reference conditions of 15oC, 1,013.25 mbar, dry. Adjustments may be needed under different conditions.

c/ A factor of 0.02388 is used to convert refinery gas in terajoules to a weight basis of thousand metric tons.

#### Standard calorific values for electricity/heat

The original unit for electricity and heat is an energy unit (mass and volume are not applicable units in this case).  Thus there is no need for standard conversion factors for electricity and heat, but rather a table of equivalence between energy units (e.g., GWh to TJ, toe, Gcal, etc.), which is presented in Table 10 in Annex.

#### Standard calorific values for biomass fuels

Biomass plays an important role in the energy mix of many countries. This is particularly true in developing countries where biomass, and in particular fuelwood, is often the principal source of energy and power in rural areas. Biomass refers to several energy sources which are typically found in the informal sector. It includes fuelwood, charcoal, bagasse, and animal and vegetal wastes, but also to derived biofuels such as bioethanol and biodiesel.

Fuelwood.  In rural areas of many developing countries the principal source of energy for cooking and heating is fuelwood; yet statistics on fuelwood in general are poor.  This is due largely to the fact that fuelwood is produced and traded in the informal sector.

Fuelwood can be measured by either volume or weight.  If it is measured by volume, it can be either stacked volume or solid volume.  Measures of stacked fuelwood are the stere or stacked cubic metre and the cord (128 stacked cubic feet).  Solid volume is obtained by the water displacement method.  One advantage of measurement by volume is the relatively small influence of the moisture content of the wood on the measurement results. The weight of fuelwood is highly dependent on moisture content, and this is true for all biomass.  The more water per unit weight, the less fuelwood.  Therefore it is important that the moisture content be accurately specified when fuelwood is measured by weight.

There are two ways of measuring moisture content (mc).  They are the so-called "dry basis" and "wet basis" and are defined below.

Dry basis:

Wet basis

When biomass is very wet there is a large difference between the two moisture contents (e.g. 100 per cent mc dry basis = 50 per cent mc wet basis), but when the biomass is air-dry, the difference is small (15 per cent mc dry basis = 13 per cent mc wet basis).  It is important to state on which basis the moisture content is measured.  Most fuelwood moisture is measured on the dry basis, but some is measured on the wet basis.

Another important determinant of the energy content of fuelwood is ash content.  While the ash content of fuelwood is generally around 1 per cent, some species can register an ash content of up to 4 per cent.  This affects the energy value of the wood since the substances that form the ashes generally have no energy value.  Thus wood with 4 per cent ash content will have 3 per cent less energy content than wood with 1 percent ash content.

The standard calorific values from mass unit to energy units provided in the UN Manual F.44 are presented in Table 5.  The table shows how the calorific values vary with different moisture content of green wood, air-dried wood and oven-dried wood.

Table 5: Influence of moisture on net calorific values of standard fuelwood

(Wood with 1 per cent ash content)

|  | Percentage moisture content | Kilocalories per kilogram | Btus per pound | Megajoules per kilogram |
| --- | --- | --- | --- | --- |
|  | dry basis | Wet basis |  |  |  |
| Green wood | 160 | 62 | 1360 | 2450 | 5.7 |
|  | 140 | 59 | 1530 | 2750 | 6.4 |
|  | 120 | 55 | 1720 | 3100 | 7.2 |
|  | 100 | 50 | 1960 | 3530 | 8.2 |
|  | 80 | 45 | 2220 | 4000 | 9.3 |
|  | 70 | 41 | 2390 | 4300 | 10.0 |
| Air-dried wood | 60 | 38 | 2580 | 4640 | 10.8 |
|  | 50 a/ | 33 a/ | 2790 | 5030 | 11.7 |
|  | 40 | 29 | 3030 | 5460 | 12.7 |
|  | 30 | 23 | 3300 | 5930 | 13.8 |
|  | 25 b/ | 20 b/ | 3460 | 6230 | 14.5 |
|  | 20 | 17 | 3630 | 6530 | 15.2 |
|  | 15 | 13 | 3820 | 6880 | 16.0 |
| Oven-dried wood | 10 | 9 | 4010 | 7220 | 16.8 |
|  | 5 | 5 | 4230 | 7610 | 17.7 |
|  | 0 | 0 | 4470 | 8040 | 18.7 |

Sources:  from UN Manual F.44. the original source was: Food and Agriculture Organization, A New Approach to Domestic Fuelwood Conservation, (Rome, 1986); D. A. Tillman, Wood as an Energy Resource (New York, Academic Press, 1978); and United Nations, Concepts and Methods for the  Collection and Compilation of Statistics on Biomass Used as Energy, by K. Openshaw (ESA/STAT/AC.3016).

a/ Average of as-received fuelwood on cordwood basis (4-foot lengths).

b/ Average of logged fuelwood.

When fuelwood is collected in volume units, a conversion factor has to be used to obtain mass units.  Table 6 shows the standard conversion factors to go from volume units to mass units.  Table 12 in Annex shows how the different moisture contents of fuelwood affect the conversion factors between cubic metres and metric tons.

Table 6: Standard fuelwood conversion table

(Wood with 20–30 per cent moisture content)

| Fuel wood | Metric tons per cubic metre | Metric tons per cord | Cubic metres per metric ton | Cubic feet per metric ton |
| --- | --- | --- | --- | --- |
| General | 0.725 | 1.54 | 1.38 | 48.74 |
| Coniferous | 0.625 | 1.325 | 1.60 | 56.50 |
| Non-Coniferous | 0.750 | 1.59 | 1.33 | 46.97 |

Source: from UN Manual F.44. The original source was: Food and Agriculture Organization of the United Nations, Yearbook of Forest Products, 1983 (Rome, 1985).

Note: 1 cord of wood  =  3.624556 cubic metres  =  128 cubic feet

1 stere (stacked wood)  =  1 stacked m3  =  35.31467 stacked cubic feet

1 board foot of wood  =  2.359737 x 10-3 m3  =  0.08333 cubic feet

These tables need to be updated and revised as even the UN Manual F.44 (page 31) mentions (in relation to Tables 6 and 12) that

“Discrepancies do exist between the above two tables and this reflects much of the literature on fuelwood measurement.  It occurs in this case largely because the former is based on information contained in standardized tables while the latter presents results of more current research”

Charcoal.  The amount of biomass (usually fuelwood) necessary to yield a given quantity of charcoal depends mostly on three factors: density, moisture content and the means of charcoal production.

The principal factor in determining the yield of charcoal from fuelwood is parent wood density, since the weight of charcoal can vary by a factor of 2 for equal volumes.  However, the moisture content of the wood also has an appreciable effect on yields; the drier the wood, the greater is the yield.  The means of charcoal production is the third determinant of yield.  Charcoal is produced in earth-covered pits, in oil drums, in brick or steel kilns and in retorts.  The less sophisticated means of production generally involve loss of powdered charcoal (fines), incomplete carbonization of the fuelwood and combustion of part of the charcoal product, resulting in lower yields.

There is always an amount of powdered charcoal produced in the manufacture and transport of charcoal.  If powdered charcoal undergoes briquetting, then the weight of the briquettes may be 50-100 per cent higher, per given volume of unpowdered charcoal, due to greater density.

The three variables which affect the energy value of charcoal are: moisture content, ash content and degree of carbonization.  The average moisture content of charcoal is 5 per cent.  The average ash content of wood charcoal is 4 per cent, while that of charcoal produced from woody crop residues, such as coffee shrubs, is near 20 per cent.  With the assumption of complete carbonization, the average energy value of wood charcoal with 4 per cent ash content and 5 per cent moisture content is approximately 30.8 MJ/kg.  The average energy value of crop residue charcoal with 20 per cent ash content and 5 per cent moisture content is 25.7 MJ/kg.

Two tables are provided in the Annex pertaining to charcoal production. Table 13 illustrates the effect of parent wood density and moisture content on charcoal yield. Table 14 supplies conversion factors for production of charcoal by the various kilns for selected percentages of wood moisture content.  It assumes some standard hardwood as input to the process.

Vegetal and animal wastes.  Energy stored in agricultural wastes and waste products from food processing increasingly are being used to replace woody biomass in fuelwood deficient areas.  These waste products can be burned as fuels to fulfill heating or cooking requirements.

There are two important determinants of the energy value of non-woody plant biomass-one is moisture content and the other is ash content.  While the ash content of wood is generally around 1 per cent, that of crop residues can vary from 3 per cent to over 20 per cent, and this affects the energy value.  Generally, the substances that form the ashes have no energy value.  Thus biomass with 20 percent ash content will have 19 percent less energy than a similar substance with 1 per cent ash content. Data for these potential sources of energy are rarely collected directly but derived from crop/waste or end-product/waste ratios. Due to this wide of variability in composition, ash and moisture content of general animal and vegetal wastes across countries, it is recommended to report these products to international organizations in an energy unit (TJ preferably) rather than their natural units. Country authorities in general are able to assess and determine the energy content of these wastes. Alternatively, measuring the energy content can be accomplished by measuring the heat or electricity output of transformation devices and applying standard efficiency factors.

Given the importance of the use of bagasse, the fibrous cane residue from the production of sugar from sugar cane, possible estimation procedures shall be outlined for this case. Also, singling out this specific vegetal waste allows reporting quantities to international organizations in its natural unit (weight basis), since its composition does not allow much variation. This has been done by the international organizations who treat bagasse separately from ordinary vegetal waste. Bagasse is used as a fuel mostly for the sugar industry's own energy needs (at times excess electricity is also fed into the public grid) in many sugar-producing countries. The availability of fuel bagasse can be estimated based on either (a) data on the input of sugar cane into sugar mills, or (b) production data on centrifugal cane sugar.

Method (a):  Studies based on experiences in Central American countries, found that the yield of fuel bagasse is approximately 280 kilograms per ton of sugar cane processed.  Assuming a 50 per cent moisture content at the time of use, 1 ton of bagasse yields 7.72 GJ.  The energy values for bagasse corresponding to 1 ton of processed sugar cane are, therefore, as follows:

2.16 GJ  =  0.516 Gcal  =  0.074 tce  =  0.051 toe

Method (b):  Based on observations, the Economic Commission for Latin America and the Caribbean (ECLAC) proposed the use of 3.26 kg bagasse yield per kilogram of centrifugal sugar produced.  Calorific equivalents for bagasse corresponding to the production of 1 ton of sugar are as follows:

25.2 GJ  =  6 Gcal  =  0.86 tce  =  0.59 toe

Animal waste or dung is another important by-product of the agricultural sector.  It can be dried and burned directly as a fuel for space heating, cooking or crop drying.  When used as an input to biogas digestors, the outputs are gas for cooking, heating and lighting, and a solid residue for use as fertilizer. Another possibility is to use the animal waste as a feedstock to produce biodiesel. It can also be spread with no or minimal treatment in the fields as fertilizer. Table 15 in Annex presents various animal and vegetal wastes and indicates the approximate calorific values recoverable from them when used as fuels.

## Recommendations

[TO BE DISCUSSED]

The recommendations on “accounting units and conversion” in the UN Manual F.29 are the following (they are taken verbatim and are presented here so that they can be reviewed and amended as needed).

(Rec. 5)	National and international offices in charge of energy statistics, and bodies that advise them or undertake work for them, should always define clearly the accounting units or presentation units employed in published analyses. The conversion factors and the route used to convert original physical units into the chosen common accounting unit or units should also be stated, or readily available published sources where they may be found should be cited. It should also be made clear whether energy units are defined on a gross or net calorific basis (para.48; see also (19) and (20), below).

(19)	When expressing the energy content of primary and secondary fossil energy sources in terms of a common energy accounting unit, net calorific values (NCV) should be used in preference to gross calorific values (GCV). If and when recuperation of a significant part of the difference between GCV and NCV from exhaust gases becomes a practical possibility and seems likely to become a reality, this recommended basis may need to be reconsidered (para. 135).

(20)	Given that the joule, and multiples of it by raising it to powers of 103, is the only energy unit in the SI, international and national offices in charge of energy statistics should consider adopting the joule (1 joule = 0.239 calorie) as the accounting unit for energy balances. The toe (1 toe = 107 kcal NCV) and/or tce (l tce= 7 x 106 kcal NCV) may be used as alternative presentation units. Whenever they are used, the route used for converting original data to toe or tce should be clearly described (para. 157).

[THE FOLLOWING MAY BE RECOMMENDED – FOR DISCUSSION]

It is recommended to collect data in original units and on the specific conversion factors used in the conversion to the common units. A country-specific calorific value will arise as a weighted average of all the calorific values collected for the fuel in question. For some fuels (e.g. coal and crude oil) different calorific values may be needed for production, imports, exports and several major uses. Standard calorific values should be used only in the absence of specific ones, acknowledging that this simplification will affect the precision of the published figures.

No specific measurement unit is recommended for national data collection, to allow countries to choose the measurement units most suitable for respondents to report. However, based on common practices, units are recommended for data dissemination. Organizations and countries may use other units, as long as clear conversions factors are provided.

For each class of fuels the recommended unit for dissemination is displayed on Table 7.  Where there is no mention, it applies to primary as well as derived fuels.

Table 7: Recommended units for dissemination

|  | Dimension | Unit |
| --- | --- | --- |
| Solid fossil fuels | Mass | Thousand tons |
| Liquid fossil fuels | Mass | Thousand tons |
| (Liquid) Biofuels | Mass/Volume | Thousand tons/ Thousand cubic metres |
| Gases | Energy | Terajoules |
| Wastes | Energy | Terajoules |
| Fuelwood | Volume | Thousand cubic metres |
| Charcoal | Mass | Thousand tons |
| Electricity | Energy (power x time) | GWh |
| Electricity installed capacity | Power | MW |
| Refinery capacity | Mass/time | Thousand tons/year |
| Heat | Energy | Terajoules |
| Common unit (e.g., balances) | Energy | Terajoules |

[PLEASE COMMENT ON LIQUID BIOFUELS]

It is recommended to report to international organizations both physical quantities of fuels and their country-specific (and where necessary flow-specific) calorific values.

When the type of waste is well-defined in its constitution, rather than only by the process by which it was generated, one can assume that there should not be great variation in specific conversion factors. In this case, data can be reported on a weight basis (thousand metric tons). Even so, if the specific conversion factors are available, they should be provided. Bagasse and black liquor (also referred to as pulp and paper waste) both fall in such case.

Common units.  One tce has traditionally been defined as comprising 7 x 106 kcal and one toe as l x 107 kcal. The conversion from original units into tce or toe implies choosing coefficients of equivalence between different forms and sources of primary energy.  When using tce and toe as common unit (or any other unit based on one particular fuel for the same effect), it should not be assumed that one ton of coal has one tce or that one ton of oil has one toe of energy content. This approach could lead to distortions since there is a wide spread in calorific values among types of coal and individual petroleum products, and between calorific values of coals and crude oils in different countries.  Rather, it is recommended to treat tce and toe as the energy units they are, and thus convert data to tce and toe either directly or indirectly (by means of an intermediary energy unit; terajoules, for example), using the pertinent conversion factors.  This approach entails, for example, having different conversions factors for each grade of coal and treating them separately.

Net and Gross calorific values.  It is recommended that net (rather than gross) calorific values (NCVs rather than GCVs) are used. In other words, the heat required to evaporate moisture, which is present in all fuels (except electricity) and is also produced in the combustion process, should not be treated as part of a fuel's energy providing capability. However, where available, it is strongly encouraged reporting both gross and net calorific values.

## Annex to Chapter 4

### Complementary Tables

Table 8: Mass equivalents

| INTO FROM | Kilograms | Metric tons | Long tons | Short tons | Pounds |
| --- | --- | --- | --- | --- | --- |
|  | MULTIPLY BY |
| Kilograms | 1.0 | 0.001 | 0.000984 | 0.001102 | 2.2046 |
| Metric tons | 1000. | 1.0 | 0.984 | 1.1023 | 2204.6 |
| Long tons | 1016. | 1.016 | 1.0 | 1.120 | 2240.0 |
| Short tons | 907.2 | 0.9072 | 0.893 | 1.0 | 2000.0 |
| Pounds | 0.454 | 0.000454 | 0.000446 | 0.0005 | 1.0 |

Note:  The units of the columns can be converted into the units of the rows by dividing by the conversion factors in the table.

Example:  Convert from metric tons (ton) into long tons: 1 ton = 0.984 long ton.

Table 9: Volume equivalents

| INTO FROM | U.S. gallons | Imperial gallons | Barrels | Cubic feet | Litres | Cubic metres |
| --- | --- | --- | --- | --- | --- | --- |
|  | MULTIPLY BY |
| U.S. gallons | 1.0 | 0.8327 | 0.02381 | 0.1337 | 3.785 | 0.0038 |
| Imp. gallons | 1.201 | 1.0 | 0.02859 | 0.1605 | 4.546 | 0.0045 |
| Barrels | 42.0 | 34.97 | 1.0 | 5.615 | 159.0 | 0.159 |
| Cubic feet | 7.48 | 6.229 | 0.1781 | 1.0 | 28.3 | 0.0283 |
| Litres | 0.2642 | 0.220 | 0.0063 | 0.0353 | 1.0 | 0.001 |
| Cubic metres | 264.2 | 220.0 | 6.289 | 35.3147 | 1000.0 | 1.0 |

Note:  The units of the columns can be converted into the units of the rows by dividing by the conversion factors in the table.

Example:  Convert from barrels into cubic meters.    1  barrel = 0.159 cubic meter.

Table 10: Conversion equivalents between energy units

| INTO FROM | TJ | Million Btu | GCal | GWh | ktoe | ktce |
| --- | --- | --- | --- | --- | --- | --- |
|  | MULTIPLY BY |
| Terajoule (TJ) | 1 | 947.8 | 238.84 | 0.2777 | 2.388x10-2 | 3.411x10-2 |
| Million Btu | 1.0551x10-3 | 1 | 0.252 | 2.9307x10(4 | 2.52x10(5 | 3.6x10(5 |
| GigaCalorie (GCal) | 4.1868x10-3 | 3.968 | 1 | 1.163x10(3 | 10-4 | 1.429x10-4 |
| Gigawatt hour (GWh) | 3.6 | 3412 | 860 | 1 | 8.6x10-2 | 1.229x10-1 |
| ktoe | 41.868 | 3.968x104 | 104 | 11.630 | 1 | 1.429 |
| ktce | 29.308 | 2.778x104 | 0.7x10-4 | 8.14 | 0.7 | 1 |

Note:  The units of the columns can be converted into the units of the rows by dividing by the conversion factors in the table.

Example:  Convert from Gigawatt-hours (GWh) into Terajoules (TJ):    1 GWh  = 3.6 TJ.

Table 11: Difference between net and gross calorific values for selected fuels

| Fuel | Percentage |
| --- | --- |
| Coke | 0 |
| Charcoal | 0 – 4 |
| Anthracite | 2 – 3 |
| Bituminous coals | 3 – 5 |
| Sub-Bituminous coals | 5 – 7 |
| Lignite | 9 – 10 |
| Crude oil | 5 – 8 |
| Petroleum products | 3 – 9 |
| Natural gas | 9 – 10 |
| Liquefied natural gas | 7 – 10 |
| Gasworks gas | 8 – 10 |
| Coke-oven gas | 10 – 11 |
| Bagasse (50% moisture content) | 21 – 22 |
| Fuelwood (10% moisture content) | 11 – 12 |
| (20% moisture content) | 22 – 23 |
| (30% moisture content) | 34 – 35 |
| (40% moisture content) | 45 – 46 |

Sources: This is taken from the UN Manual F. 44 and the original source was :[T. T. Baumeister and others, eds., Marks Standard Handbook for  Mechanical Engineers (McGraw Hill, New York, 1978); United States of America, Federal Energy Administration, Energy Interrelationships (Springfield, Virginia, National Technical Information Service, 1977); United Nations, Economic Commission for Europe, Annual Bulletin of Gas Statistics for Europe, 1983 (United Nations Publication, Sales No. E.F.R.84.II.E.28)].

Table 12: Influence of moisture on solid volume and weight of standard fuelwood

| Percentage moisture content of fuelwood |
| --- |
|  | 100 | 80 | 60 | 40 | 20 | 15 | 12 | 10 | 0 |
| Solid volume in m3 per ton | 0.80 | 0.89 | 1.00 | 1.14 | 1.33 | 1.39 | 1.43 | 1.45 | 1.60 |
| Weight in tons per m3 | 1.25 | 1.12 | 1.00 | 0.88 | 0.75 | 0.72 | 0.70 | 0.69 | 0.63 |

Source:  from UN Manual F.44.  The original source was: Food and Agriculture Organization, Wood Fuel Surveys, (Rome, 1983).

Table 13: Fuelwood to charcoal conversion table

| Influence of parent wood density on charcoal production (Weight (kg) of charcoal produced per cubic metre fuelwood) |
| --- |
|  | Coniferous wood | Average tropical Hardwoods | Preferred Tropical hardwoods | Mangrove (rhizophora) |
| Charcoal | 115 | 170 | 180 | 285 |
| Influence of wood moisture content on charcoal production (Quantity of wood required to produce 1 ton of charcoal) |
| Moisture content (dry basis) | 100 | 80 | 60 | 40 | 20 | 15 | 10 |
| Volume of wood required (cubic metres) | 17.6 | 16.2 | 13.8 | 10.5 | 8.1 | 6.6 | 5.8 |
| Weight of wood required (tons) | 12.6 | 11.6 | 9.9 | 7.5 | 5.8 | 4.7 | 4.1 |

Sources:  from UN Manual F.44.  The original source was: Wood Fuel Surveys, (Rome, 1983). D. E. Earl, Forest Energy and Economic Development (London, Oxford University Press, 1975); and the Food and Agriculture Organization of the United Nations.

Table 14: Fuelwood requirement for charcoal production by kiln type

(Cubic metres of fuelwood per ton of charcoal)

| Kiln Type | Percentage moisture content of fuelwood |
| --- | --- |
|  | 15 | 20 | 40 | 60 | 80 | 100 |
| Earth kiln | 10 | 13 | 16 | 21 | 24 | 27 |
| Portable steel kiln | 6 | 7 | 9 | 13 | 15 | 16 |
| Brick kiln | 6 | 6 | 7 | 10 | 11 | 12 |
| Retort | 4.5 | 4.5 | 5 | 7 | 8 | 9 |

Source:  from UN Manual F.44.  The original source was: Food and Agriculture Organization, Wood Fuel Surveys, (Rome, 1983).

Table 15: Energy values of selected animal and vegetal wastes

| Wastes | Average moisture content: dry basis (percentage) | Approximate ash content (percentage) | Net calorific value (MJ/ka) |
| --- | --- | --- | --- |
| Animal dung | 15 | 23-27 | 13.6 |
| Groundnut shells | 3-10 | 4-14 | 16.7 |
| Coffee husks | 13 | 8-10 | 15.5-16.3 |
| Bagasse | 40-50 | 10-12 | 8.4-10.5 |
| Cotton husks | 5-10 | 3 | 16.7 |
| Coconut husks | 5-10 | 6 | 16.7 |
| Rice hulls | 9-11 | 15-20 | 13.8-15.1 |
| Olives (pressed) | 15-18 | 3 | 16.75 |
| Oil-palm fibres | 55 | 10 | 7.5-8.4 |
| Oil-palm husks | 55 | 5 | 7.5-8.4 |
| Bagasse | 30 | 10-12 | 12.6 |
| Bagasse | 50 | 10-12 | 8.4 |
| Bark | 15 | 1 | 11.3 |
| Coffee husk, cherries | 30 | 8-10 | 13.4 |
| Coffee husk, cherries | 60 | 8-10 | 6.7 |
| Corncobs | 15 | 1-2 | 19.3 |
| Nut hulls | 15 | 1-5 | 18.0 |
| Rice straw & husk | 15 | 15-20 | 13.4 |
| Wheat straw & husk | 15 | 8-9 | 19.1 |
| Municipal garbage | . . | . . | 19.7 |
| Paper | 5 | 1 | 17.6 |
| Sawdust | 50 | 1 | 11.7 |

Sources:  from UN Manual F.44.  The original source was: G. Barnard and L. Kristoferson, Agricultural Residues as Fuel in the Third World, (London, Earth Scan, 1985); Commonwealth Science Council, Common Accounting Procedures for Biomass Resources Assessment in Developing Countries  (London, 1986); Food and Agriculture Organization of the United Nations, Energy for World Agriculture (Rome, 1979); United States of America, Federal Energy Administration, Energy Interrelationships (Springfield, Virginia, National Technical Information Service, 1977).

Note:  Two dots (..) indicate that data are not available.

### Glossary

Calorific value – measurement of the heating power of a fuel in relation to its mass or volume. It is a conversion factor between quantities of fuel expressed in mass or volume and quantities of fuel expressed in energy content. § 4.26

Common unit – In tables displaying statistics on more than one energy product (e.g., an energy balance), a common unit is usually employed to allow for inter-product comparability. It is in general an energy unit. § 4.22

Conversion factor – in the context of this chapter, any multiplying constant that can be used to convert quantities of an energy product in a given unit to its equivalent in another unit. It may be universal (e.g., to convert between two different mass units) or origin-, period- and fuel-specific (e.g., to convert from mass to energy).

Heating value – see “calorific value”.

International System of Units (SI) –modernized version of the metric system established by international agreement. § 4.4 and Box 4.1.

kilocalorie (kCal) – energy unit equivalent to 4.1868 kilojoules (1 Cal = 4.1868 J).

kilowatt-hour (kWh) – energy (work) unit suitable for measuring electricity. For example, 1 kWh is required to light a 100W bulb for ten hours (100W x 10 hours = 1000 Wh = 1 kWh).

Natural unit – see “original unit”

Original unit – units of measurement employed at the point of measurement of the product flow that are those best suited to its physical state (solid, liquid or gas) and that require the simplest measuring instruments (from IEA/Eurostat Manual page 19). § 4.6

SI – from the French “Système International d’Unités” – see “International System of Units”.

Terajoule – 1012 joules, where the joule (J) is the SI unit for heat/energy. § 4.18

Ton of coal equivalent (tce) – energy unit equivalent to the energy content of one ton of a standard-grade coal. As a convention, it is defined to be equivalent to 7 x 106 kcal.

Ton of oil equivalent (toe) – energy unit equivalent to the energy content of one ton of a standard-grade crude oil. As a convention, it is defined to be equivalent to l x 107 kcal

# Footnotes

with some exceptions; for example, fuelwood, which is usually sold in stacks and measured in a local volume unit, then converted to cubic metres.

Even though they refer to physical quantities of a standard-grade coal and crude oil.

# Comments

wasn’t sure which values you were referring to – do you mean that you want to have regional defaults for the secondary oil products in Table 2?  It doesn’t fit very well into the structure of the table…

our values are only average values – it seems that these values are more detailed so it seems worth keeping them if they are correct.

that would be very helpful

definitely better

Yes of course, although not by chapter for the whole book.

what about physical units? Is natural a proper word?

Do we want to refer to specific pages in the Manual?  If so you would need to be specific about which edition it was, because the pages could change the next time.

weight or volume.  Although production,  and prices may be in volume, consumption is usually in weight.

???

what does “given” mean?  Perhaps this needs to be redrafted.

Since Joule is the reference, I would reverse the order and say that a calorie is 4 times, etc.

change everywhere to be “Default”

We have to be very careful here since for some products the CV can vary a lot – especially for coal and natural gas.  Should we give a range?

Are there no more recent values?

ditto

ditto

ditto

ditto

ditto

charcoal does not always come from wood.  For example, some countries use coconut shells.

this is important since a lot of times it is the Energy Ministries and not the Statistical Offices.

this makes it sound as though you can only have one value per fuel – we have flow-specific values for coal and crude oil.

we ask for fuelwood in energy because of the wide range of NCVs

Is any one aware of a differernt definition of toe and/or tce?

repetitive

Iain pointed out the difference between values for NG and LNG. In case this difference really exists, he suggested having an explanation. There might be a difference in composition, if we compare wet natural gas to LNG, as the latter needs to be purified to avoid certain technical problems. Can anybody say anything about that?

No technical improvements since 1983?

Sources are from 1977 to 1985 – anything more recent?

# Text boxes

DESCRIPTION TO BE INSERTED